# ebXML Press Backgrounder

The vision of ebXML is to enable a global electronic marketplace where enterprises of any size and in any geographical location can meet and conduct business with each other through the exchange of XML based messages. ebXML enables anyone, anywhere, to do business with anyone else over the internet.

ebXML is a set of specifications that together enable a modular, yet complete electronic business framework. If the Internet is the information highway for electronic business, then you can think of ebXML as providing the on ramp, off ramps, and the rules of the road.

The ebXML architecture provides:

- a uniform message transport layer

- a way to define company profiles

- a way to define trading partner agreements

- a way to define business processes and their associated messages and content.

- Finally, it provides a way to register and discover process sequences with  related message structure and rules, as well as registering and discovering parties that are able to participate in such processes and message exchanges.

The ebXML initiative is designed for electronic interoperability, allowing businesses to find each other, agree to become trading partners and conduct business. All of these operations can be performed automatically, minimizing, and in almost all cases completely eliminating, the need for human intervention. This streamlines business to business eCommerce through a low cost, open standard mechanism.

ebXML is global in support, scope and implementation. It is a joint initiative of the United Nations (UN/CEFACT) and OASIS, developed with global participation for global usage. This partnership brings a great deal of credibility to ebXML, representing major vendors and users in the IT industry and support from leading vertical and horizontal industry groups including RosettaNet, GCI, OTA, and many others. Membership in ebXML is open to anyone and the initiative enjoys broad industry support with over  member companies, and in excess of 1,400 participants drawn from over 30 countries. ebXML also has a well defined technical scope and a set delivery timeline of 18 months (May 2001) in which to complete the full set of technical specifications. Some specifications, such as the Transport, Routing, and Protocol (TR&P), are available for developers to begin working with now. Other specifications are currently going through a public comment period and will be available soon.

ebXML is evolutionary, not revolutionary.  It is based on Internet technologies using proven, public standards such as: HTTP, TCP/IP, mime, smtp, ftp, UML, and XML. The use of public standards yields a simple and inexpensive solution that is open and vendor-neutral. ebXML can be implemented and deployed on any platform in any language. The end result is a straightforward, robust solution with low cost of adoption.  Businesses of all sizes are likely to adopt ebXML for these reasons of cost and ease of use.

Electronic commerce is not a new concept. For the past 25 years, companies have been exchanging information with each other electronically, based on a set of EDI standards defined by UN/CEFACT. Unfortunately, EDI requires significant technical expertise, deploys tightly coupled implementations, and requires the use of expensive private networks to conduct business with each other. As a result, EDI usage has been limited to only the largest enterprises, which represents a small fraction of the world's business entities. ebXML will remove these obstacles, opening the possibility of low cost electronic business to virtually anyone with a computer and an application that is capable of reading and writing ebXML messages. Businesses of all sizes are likely to adopt ebXML for these reasons of low cost and ease of use.

ebXML is now. Although  the complete set of ebXML specifications will be finished by May 2001, developers can begin working with ebXML now. The Transport, Routing, and Packaging specification has gone through several drafts and proof of concept demonstrations and is stable enough to be used for early development work. ebXML is an end-to-end solution, but it is modular in nature. Businesses are not required to implement the entire specification all at once. Specification sets may be implemented incrementally as needed. The specification sets, each being stand-alone, but all of them being aligned with each other, can be implemented individually or in a number of useful combinations, to provide complementary value to already existing eCommerce approaches.

As the world adopts ebXML, barriers to participation in global eCommerce will fall away. Virtually free transport will be available over the internet. Standards based process and message definitions will drastically reduce the cost of negotiating trading partner agreements (TPA's). ebXML compliant off-the-shelf software will enable any company, however low-tech, to easily implement their participation in ebXML based eCommerce.

The ebXML enabled world is one of mixed small, medium and large sized enterprises conducting business with each other in much more standard and low cost ways than today. Numerous opportunities will exist for all businesses to move to new, innovative, service based business models, without having to fundamentally change existing architecture or software.

Architectural overview

In order for enterprises to conduct business with each other they must:

- Find out about each other’s existence and what products and services they can offer each other

Determine which shared process and its associated information exchanges to use for obtaining these products or services from each other

- Determine the contact points and form of communication for the exchange of information

- Agree on the contractual terms (TPA) on the above chosen processes and associated information, as well as contact points and form of communication for such products or service exchanges

And then they can:

- Exchange information and services according to the above agreements.

ebXML is designed to solve these problems, built on three basic concepts: provide an infrastructure that ensures electronic interoperability, a semantics framework that ensures commercial interoperability, and a marketplace that allows enterprises to find each other, agree to become trading partners and conduct business with each other.

- Infrastructure to ensure electronic interoperability is provided through:

- message transport mechanism with a standard, well defined interface, standard

packaging rules, and predictable delivery and security

b) ‘business service interface’, i.e. a piece of software that sits at either end of the

transport and handles incoming and outgoing messages

- integration to existing back office applications. This is currently out of scope of

ebXML proper, but probably represents both the biggest challenge and the biggest

opportunity for software providers.

2.   Semantic Framework to ensure commercial interoperability is provided through:

a)  metamodel for defining business process and information models

b)  set of re-useable business objects based on core components that reflect the business knowledge.

c)  process for defining actual message structures and message structure definitions as they relate to the activities in the Business Process model.

- Marketplace to allow enterprises to find each other, agree to become trading partners,

and conduct business, is provided through:

- shared repository where enterprises can register and discover each other’s business services via the profile information

- process for defining and agreeing to a formal Trading Partner Agreement (TPA), if so desired or where required

Access to the repository for company profiles and business process models including the related message structures.

- The ebXML architecture is described in the following diagram:

ebXML Technical Architecture

The technical architecture is composed of five main specifications:

- Business Process and Information Model

- Company profiles

- Transport/Packaging & routing

- Registry & Repository

- Trading Partner Agreements

The Business Process models define how business processes are described. Business Processes represent the “verbs” of eCommerce and can be represented using UML.

The Information models define reusable components/objects that can be applied in a standard way regardless of business data. Business Objects (Core components) represent the nouns” of eCommerce.  They are defined using identity items that are common across all businesses. This enables users to define data that is meaningful to their business while also maintaining interoperability with other businesses.

The Transport Routing and Packaging (TR&P) specification defines the set of services and protocols that enables an e-commerce client to request services from e-commerce servers. The specification does not require the use of a specific protocol, rather any application-level protocol can be used. This can include common protocols such as SMTP, HTTP, FTP. Digital signatures can be applied to individual messages or a group of related messages to guarantee authenticity. Secure protocols such as HTTPS can be used to guarantee confidentiality.

The Registry and Repository specification defines the functional requirements and interfaces to a registry and repository. The repository has three functions.

- For the standards developer it will store not only the final business process definitions and its related information (message definitions), but also the core components and business objects.

- For the implementers it stores in addition to the business process and information models also the complete set of ebXML specifications

- For the user (application) it stores company profiles and gives access to all business prcoesses and information models to allow updates and addition over time.

## The Trading Partner specification defines the technical parameters of the trading partner profiles and trading partner agreements (TPA). This captures critical information for communications between applications and business processes. This also records specific technical parameters for conducting electronic commerce. The specification is based on work previously proposed by OASIS and CommerceNet.

## ebXML Adoption Scenario

As with any specification, a maturity cycle for enterprises and software providers is anticipated.. Some of the ebXML specifications may be used more extensively than others in early implementations.

Most likely, transport implementations in accordance to the ebXML Transport specification will emerge. Following close after, ‘adaptor’ implementations that comply with the ebXML TPA specification will appear. Adaptor implementations will be capable of both receiving and sending messages as well as interacting accordingly with an enterprise's internal business systems.

The next area of likely implementation is that groups of enterprises will either register business process and information models based on existing sets of message structure definitions. Application vendors will start providing applications that comply with such sets of process models and message structures. These applications will be capable of sending and receiving messages from the transport.

More mature adopters of the ebXML specifications will agree on the modeling of B2B processes and register them for re-use according to the ebXML Business Process and Information specification. Beyond that, mature adopters will start augmenting their processes with formal definitions of contractual terms according to the ebXML Business Process specification.

As a number of discrete processes evolve, patterns will emerge. These patterns themselves can be defined and registered, and can be used for definition of future processes. Some such patterns have already been discovered and defined in many business models.

## When a group of enterprises have adopted all the ebXML specifications and are using off-the-shelf or homegrown compliant software, they will be able to conduct all the six steps of doing business electronically and seamlessly, with partners across the globe, without major technical or financial entry barriers.

ebXML Deliverables Timeline

The duration of the ebXML effort has been defined as an 18 month period, beginning in November 1999 and ending in May 2001. The five core technical specifications outlined below will be delivered in final form by May 2001, with proof of concept demonstrations along the way. These specifications are developed in a totally open forum, with input from any ebXML member and approved by vote of the full membership plenary.

The specifications will likely be completed in a modular fashion on a time phased basis, as opposed to the delivery of a monlithic single specification. It is not necessary to wait until May 2001 to begin implementing components of the ebXML architecture.

## Summary

ebXML is a set of specifications that enable a complete eCommerce framework. ebXML is a global initiative aimed at solving global problems. It is an 18 month effort supported by the UN and OASIS. ebXML is a low cost, evolutionary solution using proven, open standards such as TCP/IP, HTTP, and XML,aimed at businesses of all sizes and can be implemented with a minimum of training and education. ebXML is a modular, end to end solution that can work with existing eCommerce solutions such as EDI.

The ebXML global electronic marketplace is built on an infrastructure that ensures electronic interoperability. This is accomplished through a semantics framework and an actual marketplace that allows enterprises to find each other, agree to become trading partners and actually conduct business with each other. ebXML will enable the evolution of many new business models and through business process patterns and the ‘commoditization’ of such business models. ebXML enables anyone, anywhere to do business with anyone else over the Internet, adding greater productivity to, and expanding, the global electronic economy.

# Comments

The Initiative is call eb NOT eC.  So let’s use the right word. Remember, eC is more along the lines of web to business, or C2B, whereas eB is B2B, application to application.

I take it most of this is based on Karstens’s vision.  I had a long talk with him on this yesterday and we came to an agreement NOT to use publicly at this time his view of the future but go with the more stable approach as seen by many industries.  Therefore many of the suggestion I am now making is along those lines.  This is consistent with the two slides showing the overall view of ebXML.

It is true one can stage the implementation of ebXML, such as Transport, Models and Repository, one can NOT separate data from process. Therefore instead of using the term components, which also conflicts with core components I use the term “sets”, such as a set of messaging & routing, registry & repository, and business process & information model standards.

The buttom-up approach as introduced here is against all modeling principles. Again, I spoke with Karsten about this. And we came to an agreement as expressed by my notes. Further, I am aware of Jon Bozak’s efforts as well. So let me try to set the stage on this one since this separation idea is reflected in a few spots in this document.

Business Process Modeling is a top-down approach. We identify the processes and the data required. Therefore we can not separate the two. As you see from slide two of the ebXML overview, the defining of the data is done in two steps, first at the conceptual level using a Lexicon that reflects the business view and in the final stage harmonized across models and industries via business objects. It is at this level that we group objects into ebXML messages that are part of a certain process. There is no separation to first implement messages made up from the conceptual core components as defined in the Lexicon.

In regard to phase 2 as seen by Jon Bosak, there will be users that want ONLY XML DTDs. They don’t want or like the process models. We will cater to them by using the message structures as identified in ebXML business models to create DTDs, but that is not what we want to push now. This is a low-key effort to be used as a migration path.

Reflecting on my comments #2 & 3, this section needs to be aligned the most, In summary, the order is process than data and the two can not be separated.

Further the idea of assembling messages at run time is a possibility, but it is in the future and not for this phase. There is a) currently not enough support for it and b) the whole concept of profile and TPA is much more complex to allow changes on the fly.

Please use the updated slide that includes the profile registration and download. I also recommend not to delete the text associated with the arrows.

Based on slide 2 of the ebXML Overview, Core components are used to express the business knowledge during the requirements and analysis phase. The harmonization, resulting in the final class diagrams, is done by creating corresponding business objects. This is reflected in the corrections to this paragraph.

I don’t like us using the term choreography. It assumes that one puts in sequence things that were independently created. In “modeling” one does the opposite, things are related and are a result of each other. Let’s use modeling instead. I know it is only marketing, but…

# Text boxes

Final

Spec

P.O.C.

Draft

Spec

P.O.C.

Final

P.O.C.

P.O.C.

P.O.C.

Final

P.O.C.

Final

P.O.C.

P.O.C.

Draft

Spec

Final

Spec

Draft

Spec

Final

P.O.C.

Draft

Spec

Final

Spec

Retrieval of ebXML Specifications & Models

UML to XML conversion

TPA

Registration

Final

Spec

ebXML

Requirements

Draft

Spec

Final

P.O.C.

Final

Spec

Open Comment Period

Trading

Partner

Build

Business Process and Information Models

Implementers

Repository

Registry &

Repository

Transport

Routing/Pkg

Core

Components

Business

Processes

Final

Spec

Shrink-wrap

Application

Internal

Business App

Business

Service

Interface

Business

Service

Interface

Transport

Message

Payload

Vienna

May 2001

Vancouver

Feb 2001

Tokyo

Nov 2000

Retrieval of new or updated ebXML Models

Retrieval of new or updated ebXML Models

Build

Draft

Spec

San Jose,

Aug 2000

Brussels

May 2000

Orlando

Feb 2000

ebXML Timeline