Messaging Service Specification

ebXML Transport, Routing & Packaging

Version 0.9

20 December 2000

# Status of this Document

This document specifies an ebXML DRAFT for the eBusiness community Distribution of this document is unlimited.

The document formatting is based on the Internet Society’s Standard RFC format converted to Microsoft Word 2000 format,

This version

http://www.ebxml.org/working/project_teams

Latest version

http://www.ebxml.org

Previous version

http://www.ebxml.org/…

# ebXML Participants

The authors wish to acknowledge the support of the members of the Transport, Routing an Packaging Project Team who contributed ideas to this specification by the group’s discussion email list, on conference calls and during face-to-face meeting.

Ralph Berwanger – bTrade.com

Jonathan Borden – Author of XMTP

Jon Bosak – Sun Microsystems

Marc Breissinger – webMethods

Dick Brooks – Group 8760

Doug Bunting – Ariba

David Burdett – Commerce One

Len Callaway – Drummond Group, Inc.

David Craft – VerticalNet

Philippe De Smedt – Viquity

Lawrence Ding – WorldSpan

Rik Drummond – Drummond Group, Inc. (Representing XML Solutions)

Christopher Ferris – Sun Microsystems

Maryann Hondo – IBM

Jim Hughes – Fujitsu

John Ibbotson – IBM

Ian Jones – British Telecommunications

Ravi Kacker – Kraft Foods

Nick Kassem – Sun Microsystems

Henry Lowe – OMG

Jim McCarthy – webXI

Bob Miller – GSX

Dale Moberg – Sterling Commerce

Joel Munter – Intel

Farrukh Najmi – Sun Microsystems

Akira Ochi – Fujitsu

Masayoshi Shimamura – Fujitsu

Kathy Spector – Extricity

Nikola Stojanovic – Columbine JDS Systems

Gordon Van Huizen – Process Software

Martha Warfelt – Daimler Chrysler

Prasad Yendluri – Vitria

# Table of Contents

1	Status of this Document	2

2	ebXML Participants	3

3	Table of Contents	4

4	Introduction	8

4.1	Summary of Contents of Document	8

4.2	Document Conventions	8

4.3	Audience	9

4.4	Related Documents	9

5	Design Objectives	10

6	System Overview	11

6.1	What the Message Service does	11

6.2	Message Service Overview	11

7	Packaging Specification	13

7.1	Introduction	13

7.1.1	ebXML Header Envelope and Payload Envelope	13

7.1.2	MIME usage Conventions	14

7.2	ebXML Message Envelope	14

7.2.1	Content-Type	14

7.2.1.1	type Attribute	14

7.2.1.2	boundary Attribute	14

7.2.1.3	version Attribute	14

7.2.2	ebXML Message Envelope Example	14

7.3	ebXML Header Container	15

7.3.1	Content-ID	15

7.3.2	Content-Type	15

7.3.2.1	version Attribute	15

7.3.2.2	charset Attribute	15

7.3.3	ebXML Header Envelope Example	16

7.4	ebXML Payload Container	16

7.4.1	Content-ID	16

7.4.2	Content-Type	16

7.4.3	Example of an ebXML MIME Payload Container	17

8	Header Document	18

8.1	XML Prolog	18

8.1.1	XML Declaration	18

8.1.2	Encoding Declaration	18

8.1.3	Standalone Document Declaration	18

8.1.4	Document Type Declaration	18

8.2	ebXMLHeader Element	19

8.2.1	ebXMLHeader attributes	19

8.2.1.1	Namespace attribute	19

8.2.1.2	version attribute	19

8.2.2	ebXMLHeader elements	19

8.2.3	Combining Principal Header Elements	19

8.2.3.1	Manifest element	19

8.2.3.2	Header element	20

8.2.3.3	RoutingHeaderList element	20

8.2.3.4	ApplicationHeaders element	20

8.2.3.5	MessageStatus Request element	20

8.2.3.6	ErrorList element	20

8.2.3.7	Acknowledgment element	20

8.2.3.8	Signature element	20

8.2.3.9	#wildcard element content	20

8.2.4	ebXMLHeader sample	20

8.3	Manifest element	21

8.3.1	Reference element	21

8.3.1.1	Description element	21

8.3.1.2	Schema element	22

8.3.2	Manifest sample	22

8.4	Header element	22

8.4.1	From and To elements	22

8.4.2	CPAId element	23

8.4.3	ConversationId element	23

8.4.4	Service element	23

8.4.4.1	ebXML Message Service Header namespace	23

8.4.5	Action element	23

8.4.6	Description element	23

8.4.7	ReliableMessagingInfo element	23

8.4.8	MessageData element	24

8.4.8.1	MessageId element	24

8.4.8.2	TimeStamp element	24

8.4.8.3	RefToMessageId element	24

8.4.9	#wildcard element	24

8.4.10	Header sample	24

8.5	RoutingHeaderList element	25

8.5.1	Routing Header Element	25

8.5.1.1	SenderURI element	25

8.5.1.2	ReceiverURI element	25

8.5.1.3	ErrorURI element	25

8.5.1.4	Timestamp element	25

8.5.1.5	#wildcard	25

8.5.2	Single Hop Routing Header Sample	26

8.5.3	Multi-hop Routing Header Sample	27

8.6	ApplicationHeaders Element	27

8.6.1	ApplicationHeaders sample	28

8.7	StatusData Element	28

8.8	ErrorList Element	28

8.8.1	id attribute	29

8.8.2	highestSeverity attribute	29

8.8.3	Error element	29

8.8.3.1	codeContext attribute	29

8.8.3.2	errorCode attribute	29

8.8.3.3	severity attribute	29

8.8.3.4	location attribute	29

8.8.3.5	errorMessage atttribute	30

8.8.3.6	softwareDetails attribute	30

8.8.4	Examples	30

8.8.5	errorCode values	30

8.8.6	Reporting Errors in the ebXML Header Document	30

8.8.7	Non-XML Document Errors	31

8.9	Acknowledgment Element	31

8.9.1	TimeStamp element	32

8.9.2	From element	32

8.9.3	type attribute	32

8.9.4	signed attribute	32

8.10	Signature Element	32

9	Message Service Handler Services	33

9.1	Message Status Request Service	33

9.1.1	Message Status Request Message	33

9.1.2	Message Status Response Message	33

9.1.3	Security Considerations	34

9.2	Message Service Handler Ping Service	34

9.2.1	Message Service Handler Ping Message	34

9.2.2	Message Service Handler Pong Message	34

9.2.3	Security Considerations	35

10	Reliable Messaging	36

10.1.1	Persistent Storage and System Failure	36

10.1.2	Methods of Implementing Reliable Messaging	36

10.2	ebXML Reliable Messaging Protocol	36

10.2.1	Single-hop Reliable Messaging	37

10.2.1.1	Resending Lost Messages	38

10.2.1.2	Duplicate Acknowledgment Messages	39

10.2.2	Multi-hop Reliable Messaging	40

10.2.2.1	Multi-hop Reliable Messaging without Intermediate Acknowledgments	40

10.2.2.2	Multi-hop Reliable Messaging with Intermediate Acknowledgments	41

10.3	ebXML Reliable Messaging using Queuing Transports	42

10.4	Failed Message Delivery	43

10.5	Reliable Messaging Parameters	44

10.5.1	Who sets Message Service Parameters	44

10.5.2	From Party Parameters	45

10.5.2.1	Delivery Semantics	45

10.5.2.2	Delivery Receipt Requested	46

10.5.2.3	Time To Live	46

10.5.3	To Party Parameters	47

10.5.3.1	DeliveryReceiptProvided	47

10.5.4	Sending MSH Parameters	47

10.5.4.1	Reliable Messaging Method	47

10.5.4.2	Intermediate Ack Requested	47

10.5.4.3	Timeout Parameter	48

10.5.4.4	Retries Parameter	48

10.5.4.5	RetryInterval Parameter	48

10.5.4.6	Deciding when to resend a message	48

10.5.5	Receiving MSH Parameters	48

10.5.5.1	Reliable Messaging Methods Supported	48

10.5.5.2	PersistDuration	48

10.5.5.3	msh Time Accuracy	49

11	Error Reporting and Handling	50

11.1	Definitions	50

11.2	Types of Errors	50

11.3	When to generate Error Messages	50

11.3.1	Security Considerations	50

11.4	Identifying the Error Reporting Location	50

12	Security	52

12.1	Security and Management	52

12.2	Unauthorized Access	52

12.3	Data Integrity and Confidentiality	52

12.4	Denial-of Service	52

12.4.1	ebXML Message Countermeasures for Denial of Service	52

12.4.2	ebXML Management Countermeasures for Denial of Service	53

12.5	Digital Certificates	53

12.6	XML Digital Signature (XMLDSIG)	53

12.6.1	Profile - XMLSignature signing of header and/or payload	53

12.6.1.1	Risks	53

12.6.1.2	Benefits	54

12.7	S/MIME	54

12.7.1	Profile - S/MIME signing of message payload	54

12.7.1.1	Sample S/MIME signed payload	54

12.7.1.2	Risks	55

12.7.1.3	Benefits	55

12.7.2	Profile - S/MIME encryption of message payload	55

12.7.2.1	Risks	55

12.7.2.2	Benefits	56

12.8	PGP/MIME	56

12.8.1	Profile - PGP/MIME signing of message payload	56

12.8.1.1	Risks	56

12.8.1.2	Benefits	56

12.8.2	Profile - PGP/MIME encryption of message payload	56

12.8.2.1	Risks	56

12.8.2.2	Benefits	56

13	Synchronous and Asynchronous Responses	57

14	References	58

15	Disclaimer	59

16	Contact Information	60

Appendix A	Schema and Data Type Definitions	62

A.1	Schema Definition	62

A.2	Data Type Definition	62

Appendix B	Examples	63

Appendix C	Communication Protocol Interfaces	64

C.1	HTTP	64

C.1.1	Asynchronous HTTP	64

C.1.2	Synchronous HTTP	65

C.2	SMTP	66

C.3	FTP	67

C.4	Communication Protocol Errors during Reliable Messaging	67

Appendix D	Reliable Messaging Processing Logic	68

Copyright Statement	69

# Introduction

This is a draft standard for trial implementation. The specification is the first in a series of phased deliverables. This version of the specification does not address service interfaces. This is being developed as separate document and will be included in a later version or as additional specifications to the ebXML Message Services Specification.

## Summary of Contents of Document

This specification defines the ebXML Message Service protocol that enables the secure and reliable exchange of messages between two parties. It includes descriptions of:

the ebXML Message structure used to package ebXML Messages for transport between parties

the behavior of the Message Service that sends and receives those messages.

No assumption or dependency is made relative to communication protocol or type of payload. The specifications contained here are both payload and communication protocol neutral.

This specification is organized around the following topics:

Packaging Specification - A description of how to package an ebXML Message and its associated parts (section 7)

Message Headers - A specification of the structure and composition of the information necessary for an ebXML Message Service to successfully generate or process an ebXML compliant message (section 8)

Message Service Handler Services – A description of two services that enable one service to discover the status of another Message Service Handler or an individual message (section 9)

Reliable Messaging - The Reliable Messaging function defines an interoperable protocol such that any two Message Service implementations can “reliably” exchange messages that are sent using “reliable messaging” semantics (section 9.2.3)

Error Handling - This section describes how one ebXML Message Service reports errors it detects to another ebXML Message Service (section 11)

Security - This version of the specification provides complete specification of the security requirements for ebXML Messages (section 12).

Appendices to this specification cover the following:

Appendix A Schemas and DTD Definitions

Appendix B Examples

Appendix C Communication Protocol Envelope Mappings

Appendix D Reliable Messaging Protocol Logic

## Document Conventions

Terms in Italics are defined in the ebXML Glossary of Terms [Glossary]. Terms listed in Bold Italics represent the element and/or attribute content of the XML ebXML Message Header. Terms listed in Courier font relate to MIME components.

The keywords MUST, MUST NOT, REQUIRED, SHALL, SHALL NOT, SHOULD, SHOULD NOT, RECOMMENDED, MAY, and OPTIONAL, when they appear in this document, are to be interpreted as described in RFC 2119 [Bra97].

Note that the force of these words is modified by the requirement level of the document in which they are used.

MUST: This word, or the terms “REQUIRED” or “SHALL”, means that the definition is an absolute requirement of the specification.

MUST NOT: This phrase, or the phrase “SHALL NOT”, means that the definition is an absolute prohibition of the specification.

SHOULD: This word, or the adjective “RECOMMENDED”, means that there may exist valid reasons in particular circumstances to ignore a particular item, but the full implications must be understood and carefully weighed before choosing a different course.

SHOULD NOT: This phrase, or the phrase “NOT RECOMMENDED”, means that there may exist valid reasons in particular circumstances when the particular behavior is acceptable or even useful, but the full implications should be understood and the case carefully weighed before implementing any behavior described with this label.

## Audience

The target audience for this specification is the community of software developers who will implement the ebXML Message Service.

It is assumed that the reader has an understanding of transports, MIME and XML.

## Related Documents

The following set of related specifications will be delivered in phases:

ebXML Collaboration Protocol Profile and Agreement Specification (under development) - defines how one party can discover and/or agree upon the information that party needs to know about another party prior to sending them a message that complies with this specification

ebXML Message Service Interface Specification (to be developed) - defines an interface that may be used by software to interact with an ebXML Message Service

ebXML Message Services Security Specification (under development) – defines the security mechanisms necessary to negate anticipated, selected threats

ebXML Message Services Requirements Specification – defines the requirements of the Message Services

# Design Objectives

The design objectives of this specification are to define a Message Service (MS) to support XML based electronic business between small, medium and large enterprises. This specification is intended to enable a low cost solution, while preserving a vendor's ability to add unique value through added robustness and superior performance. It is the intention of the Transport, Routing and Packaging Project Team to keep this specification as straightforward and succinct as possible.

Every item in this specification will be prototyped by the ebXML Proof of Concept Team in order to ensure the clarity and accuracy of this specification.

# System Overview

This document defines the ebXML Message Service (MS) component of the ebXML infrastructure. The ebXML Message Service defines the message enveloping and header document schema used to transfer ebXML Messages over a data communication mechanism such as HTTP, SMTP, etc. This document provides sufficient detail to develop software for the packaging, exchange and processing of ebXML Messages.

## What the Message Service does

The ebXML Message Service defines robust, yet basic, functionality to transfer messages using various existing communication protocols. The ebXML Message Service will perform in a manner that will allow for reliability, persistence, security and extensibility.

The ebXML Message Service is provided for environments requiring a robust, yet low cost solution to enable electronic business. It is one of the three "infrastructure" components of ebXML that includes: Registry/Repository, Collaboration Protocol Profile/Agreement (CPP/CPA) and the ebXML Message Service.

## Message Service Overview

The ebXML Messaging Service may be conceptually broken down into three parts: (1) an abstract Service Interface, (2) functions provided by the Messaging Service Layer, and (3) the mapping to underlying transport service(s).

The following diagram depicts a logical arrangement of the functional modules that exist within the ebXML Messaging Services architecture. These modules are arranged in a manner to indicate their inter-relationships and dependencies.

Figure 6-1 Typical Relationship between ebXML MSH Components

<DB>An explanation of these components is needed</DB>

# Packaging Specification

## Introduction

An ebXML Message consists of:

an outer Communication Protocol Envelope, such as HTTP or SMTP,

an inner communication “protocol independent” ebXML Message Envelope, specified using MIME multipart/related, that contains the two main parts of the Message:

an ebXML Header Container that is used to envelope one ebXML Header Document,

an optional, single ebXML Payload Container that MUST be used to envelope the actual payload (transferred data) of the Message  Communication Protocol Envelope (SMTP, HTTP, etc)

Figure 7-1 ebXML Message Structure

### ebXML Header Envelope and Payload Envelope

An ebXML Header Envelope and an ebXML Payload Envelope are constructed of standard, MIME components.

An ebXML Header (or Payload) Document is the content of the standard MIME part and is:

an XML document in an ebXML Header, or

an XML or some other document for the ebXML Payload

Any special considerations for the usage of the ebXML Message Envelope in TCP/IP, HTTP and SMTP transports are described in Appendix E.

### MIME usage Conventions

Values associated with MIME header attributes are valid in both quoted and unquoted form. For example, the forms type="ebxml" and type=ebxml are both valid.

## ebXML Message Envelope

The MIME structured ebXML Message Envelope is used to identify the message as an ebXML compliant structure and encapsulates the header and payload in MIME body parts. It MUST conform to [RFC2045] and MUST contain a Content-Type MIME header.

### Content-Type

The MIME Content-Type MUST be set to multipart/related for all ebXML Message Envelopes. See Appendix C for selection rationale. For example:

Content-Type: multipart/related;

The MIME Content-Type header contains three attributes:

type

boundary

version

#### type Attribute

The MIME type attribute is used to identify the ebXML Message Envelope as an ebXML compliant structure. It conforms to a MIME XML Media Type [XMLMedia] and MUST be set to "application/vnd.eb+xml". This new media type is derived from the application/xml type and shares many semantics with that type. To that type, application/vnd.eb+xml adds a specific application context, the ebXML Message Service. For example:

type="application/vnd.eb+xml"

#### boundary Attribute

The MIME boundary attribute is used to identify the body part separator used to identify the start and end points of each body part contained in the message. The MIME boundary SHOULD be chosen carefully in order to ensure that it does not occur within the content area of a body part see [RFC 2045] for guidance on how to do this. For example:

boundary:="-------8760"

#### version Attribute

The MIME version attribute is used to identify the particular version of ebXML Message Envelope being used. All message headers SHOULD USE "0.8". For example:

version="0.8"

### ebXML Message Envelope Example

An example of a compliant ebXML Message Envelope header appears as follows:

Content-Type: multipart/related; type="application/vnd.eb+xml";"boundary:="-------8760";

## ebXML Header Container

The ebXML Header Container is a MIME body part that MUST consist of:

one XML based ebXML Header Envelope, and

one XML ebXML Header Document (described in section 8 of this document)

The following rules apply:

the ebXML Header Container MUST be the first MIME body part in the ebXML Message.

there MUST be one and only one XML ebXML Header Document in each ebXML Message. However, an ebXML Payload Container may be a completely encapsulated ebXML Message.

The MIME based ebXML Header Envelope conforms to [RFC 2045] and MUST consist of the following MIME headers:

Content-ID

Content-Type

### Content-ID

The Content-ID MIME header identifies this instance of an ebXML Message header body part. The value for Content-ID SHOULD be a unique identifier, in accordance with RFC 2045. For example:

Content-ID: <2000-0722-161201-123456789@ebxmlhost.realm>

### Content-Type

The MIME Content-Type for an ebXML header is identified with the value “application/vnd.eb+xml". Content-Type contains two attributes:

version

charset

#### version Attribute

The MIME version attribute indicates the version of the ebXML Message Service Specification to which the ebXML Header Document conforms. For example:

version="0.8";

#### charset Attribute

The MIME charset attribute identifies the character set used to create the ebXML Header Document (an XML document that is the content of this MIME entity). The semantics of this attribute are described in [charset parameter / encoding considerations] of application/xml as specified in [XML/Media]. The list of valid values can be found at http://www.iana.org/.

If both are present, the MIME charset attribute SHALL be equivalent to the encoding declaration of the ebXML Header Document (see section 8). If provided, the MIME charset attribute MUST NOT contain a value conflicting with the encoding used when creating the ebXML Header Document. For maximum interoperability it is RECOMMENDED that [UTF-8] be used when encoding this document. Due to the processing rules defined for media types derived from application/xml [XMLMedia], this MIME attribute has no default. For example:

charset="UTF-8"

### ebXML Header Envelope Example

The following represents an example of an ebXML Header Envelope and ebXML Header

Document:

Content-ID: ebxmlheader-123@ebxmlhost.realm --|    MIME ebXML    |

Content-Type: application/vnd.eb+xml;         | Header Envelope  |

version=”0.9”; charset=”UTF-8”              --|                  | ebXML

| Header

<ebXMLHeader>                    -------------|                  | Container

<Manifest>........                          | XML ebXML Header |

</Manifest>                                 |     Document     |

<Header>........                            |                  |

</Header>                                   |                  |

<Routing Header>........                    |                  |

</Routing Header>                           |                  |

</ebXMLHeader>                   -------------|                  |

A complete example of an ebXML Header Container is presented in Appendix B. That example includes the charset attribute and portions of an XML Prolog (see sect 8.1), none of which is required to appear in an ebXML Header Container or ebXML Header Document.  Appendix B also includes the outer ebXML Message Envelope and a complete (valid) ebXMLHeader element rather than the outline shown above.

## ebXML Payload Container

If the ebXML Message contains a payload, then a single ebXML Payload Container MUST be used to envelop it.

If there is no payload within the ebXML Message then the ebXML Payload Container MUST not be present.

The contents of the ebXML Payload Container MUST be identified by the Message Manifest element within the ebXML Header Document (see section 8.3).

If the Message Manifest is an empty XML element, the ebXML Payload Container MUST NOT be present in the ebXML Message.

If an ebXML Payload Container is present, it MUST conform to MIME [RFC2045] and MUST consist of:

a MIME header portion - the ebXML Payload Envelope, and

a content portion - the payload itself that may be of any valid MIME type.

The ebXML MIME Payload Envelope, MUST consist of the following MIME headers:

Content-ID

Content-Type

The ebXML Message Service Specification makes no provision, nor limits in any way the structure or content of payloads. Payloads MAY be a simple-plain-text-object or complex nested multipart objects. This is the implementer’s decision.

### Content-ID

The Content-ID MIME Header is used to uniquely identify an instance of an ebXML Message payload body part. The value for Content-ID SHOULD be a unique identifier, in accordance with MIME [RFC 2045]. For example:

Content-ID: <2000-0722-161201-123456789@ebxmlhost.realm>

### Content-Type

The MIME Content-Type for an ebXML payload is determined by the implementer and is used to identify the type of data contained in the content portion of the ebXML Payload Container. The MIME Content-Type MUST conform to [RFC2045]. For example:

Content-Type: application/xml

### Example of an ebXML MIME Payload Container

The following represents an example of an ebXML MIME Payload Envelope and a payload:

Content-ID: ebxmlpayload-123@ebxmlhost.realm --|                                                                 ebXML MIME      |

Content-Type: application/xml     -------------| Payload Envelope | ebXML

| Payload

<Invoice>                         -------------|                  | Container

<Invoicedata>........                        | Payload          |

</Invoicedata>                               |                  |

</Invoice>                        -------------|                  |

A complete example of the ebXML Payload Container is presented in Appendix XX.

# Header Document

The ebXML Header Document is a single [XML] document with a number of principal header-elements. In general, separate principal-header elements are used where:

different software is likely to be used to generate that header-element,

the element is not always present,

the structure of the header element might vary independently of the other header-elements, or

the data contained in the header-element MAY need to be digitally signed separately from the other header-elements.

## XML Prolog

The ebXML Header Document’s XML Prolog MAY contain an XML declaration or a document type declaration.  This specification has defined no additional comments or processing instructions that may appear in the XML prolog.  For example:

<?xml version="1.0" encoding="UTF-8"?>

<!DOCTYPE ebXMLHeader SYSTEM "level1-10122000.dtd">

<ebXMLHeader>...</ebXMLHeader>

### XML Declaration

The XML declaration MAY be present in an ebXML Header Document.  If present, it MUST contain the version specification required by the XML Recommendation [XML]: version=’1.0’ and MAY contain an encoding declaration and standalone document declaration.  The semantics described below MUST be implemented by a compliant ebXML Message Service.

### Encoding Declaration

If both are present, the XML prolog for the ebXML Header Document SHALL contain the encoding declaration that SHALL be equivalent to the charset attribute of the MIME Content-Type of the ebXML

Message Header Container (see section 7.3). If provided, the encoding declaration MUST NOT contain a value conflicting with the encoding used when creating the ebXML Header Document.  It is RECOMMENDED that UTF-8 be used when encoding the ebXML Header Document.  If the character encoding cannot be determined by an XML processor using the rules specified in section 4.3.3 of [XML], the XML declaration and its contained encoding declaration SHALL be provided in the ebXML Header Document.

NOTE: The encoding declaration is not required in an XML document according to the XML version 1.0 specification [XML].

For example:

<?xml version="1.0" encoding="UTF-8"?>

### Standalone Document Declaration

The standalone document declaration, if present, MAY appear as standalone=’yes’ if and only if all of the validity requirements specified in section 2.9 of the XML Recommendation [XML] are met.  It is RECOMMENDED that ebXML Header Documents omit this declaration.

### Document Type Declaration

When the ebXML Header Document will or may be processed by an XML processor not complaint with the XML Schema Recommendation [XMLSchema], a document type declaration containing a SYSTEM identifier of "level1-10122000.dtd" MUST be included. For example:

<!DOCTYPE ebXMLHeader SYSTEM "level1-10122000.dtd">

## ebXMLHeader Element

The root element of the XML ebXML Header Document is named ebXMLHeader. Its structure is described below.

### ebXMLHeader attributes

There are two attributes associated with the ebXMLHeader, they are:

Namespace (xmlns)

version

#### Namespace attribute

The namespace declaration (xmlns) (see [XML Namespace]) has a REQUIRED value of "http://www.ebxml.org/namespaces/messageHeader".

#### version attribute

The version attribute is required. Its purpose is to provide for future versioning capabilities. It has a default value of '0.9'.

### ebXMLHeader elements

An ebXML Header Document consists of the following principal header elements:

Manifest – an element that points any data present either in the ebXML Payload Container or elsewhere, e.g. on the web

Header – a REQUIRED element that contains routing information for the message (To/From, etc.) as well as other context information about the message

RoutingHeaderList – a REQUIRED element that contains entries that identify the Message Service Handler (MSH) that sent and should receive the message

ApplicationHeaders – an element that can be used by a process or service to include additional information that needs to be associated with the data in the ebXML Payload but is not contained within it

MessageStatusRequest – an element that is used by a MSH when requesting the status of a message that was previously sent

MessageStatusResponse – an element that is used by a MSH when responding to a request on the status of a message that was previously received

ErrorList – an element that contains a list of the errors that have been found in a message

Acknowledgment – an element that is used by a MSH to indicate that a message has been received

Signature – an element that contains a digital signature that conforms to [XMLDSIG] that signs data associated with the message

#wildcard - any namespace-qualified element content belonging to a foreign namespace

### Combining Principal Header Elements

This section describes how the various principal header elements may be used in combination.

#### Manifest element

The Manifest element MUST be present if there is any data associated with the message that is not present in the ebXML Header Document. This applies specifically to data in the ebXML Payload Container or elsewhere, e.g. on the web.

#### Header element

The Header element MUST be present in every message.

#### RoutingHeaderList element

The RoutingHeaderList element MAY be present in any message. It MUST be present if the message is being sent reliably (see section 9.2.3

#### ApplicationHeaders element

The ApplicationHeaders element MAY be present on any message except a message that contains one or more of the following:

an ErrorList element with a highestSeverity attribute set to Error. See also section 8.2.3.6

a MessageStatusRequest element

a MessageStatusResponse element

#### MessageStatus Request element

This element MUST NOT be present with the following elements:

a Manifest element

an ApplicationHeaders element,

a MessageStatusResponse element

an ErrorList element with a highestSeverity attribute set to Error. (See section 8.2.3.6.)

#### ErrorList element

If the highestSeverity attribute on the ErrorList is set to Warning, then this element MAY be present with any other element.

If the highestSeverity attribute on the ErrorList is set to Error, then this element MUST NOT be present with the following:

a Manifest element

an ApplicationHeaders element

a StatusData element

#### Acknowledgment element

An Acknowledgment element MAY be present on any message.

#### Signature element

A Signature element MAY be present on any message.

#### #wildcard element content

Any namespace-qualified element content MAY be added to provide for the extensibility of the ebXMLHeader. Extension element content MUST be namespace-qualified in accordance with [XMLNamespaces] and MUST belong to a foreign namespace. A foreign namespace is one that is NOT http://www.ebxml.org/namespaces/messageHeader.

### ebXMLHeader sample

The following is a sample ebXMLHeader document fragment demonstrating the overall structure:

<?xml version="1.0" encoding="UTF-8"?>

<ebXMLHeader xmlns=”http://www.ebxml.org/namespaces/messageHeader” Version="0.8" >

<Manifest>...</Manifest>

<Header>...</Header>

<RoutingHeaderList>…</RoutingHeaderList>

</ebXMLHeader>

## Manifest element

The Manifest element is a composite element consisting of zero or more Reference elements. Each Reference element identifies data associated with the message, whether included as part of the message, or remote resources accessible via a URL. The Manifest element, if present, SHALL be the first child element of the ebXMLHeader. It identifies the payload document(s) contained in the ebXML Message Container. The purpose of the Manifest is to make it easier to directly extract a particular document associated with the Message.

The Manifest element MAY have a single attribute: id that is an XML ID.

### Reference element

The Reference element is a composite element consisting of the following subordinate elements:

Description - a textual description of the payload object referenced by the parent Reference element

Schema - information about the schema that defines the instance document identified in the parent Reference element

#wildcard - any namespace-qualified element content belonging to a foreign namespace

The Reference element itself is an [XLINK] simple link. XLINK is presently a Candidate Recommendation (CR) of the W3C. It should be noted that the use of XLINK in this context is chosen solely for the purpose of providing a concise vocabulary for describing an association. Use of an XLINK processor or engine is NOT REQUIRED, but MAY prove useful in certain implementations.

The Reference element has the following attribute content in addition to the element content described above:

id - an optional XML ID for the Reference element

xlink:type - this REQUIRED attribute defines the element as being an XLINK simple link. It has a fixed value of 'simple'

xlink:href - this REQUIRED attribute has a value that is the URI of the payload object referenced. It SHALL conform to the [XLINK] specification criteria for a simple link.

xlink:role - this REQUIRED attribute identifies the role that the payload object referenced serves. It MUST have a value that is a valid URI in accordance with the [XLINK] specification.

xlink:label - this attribute MAY be present and SHALL be used in accordance with the [XLINK] specification.

Any other namespace-qualified attribute MAY be present. A receiving MSH MAY choose to ignore any foreign namespace attributes other than those defined above.

#### Description element

The Description is an OPTIONAL textual description of the payload object referenced by the parent Reference element. The language of the description is defined by a required xml:lang attribute. The xml:lang attribute MUST comply with the rules for identifying languages specified in [XML]. This element is provided solely for the purpose of providing a human readable description of the payload object identified by the parent Reference element.

#### Schema element

The Schema element MAY be present as a child of the Reference element. It provides a means of identifying the schema, and its version, that defines the payload object identified by the parent Reference element. It has no element or text content. The Schema element contains the following attributes:

version - a version identifier of the schema

location - the URI of the schema

### Manifest sample

The following fragment demonstrates a typical Manifest for a message with a single payload MIME body part:

<Manifest id="Manifest">

<Reference id="pay01"

xlink:href="cid:payload-1" xlink:label="PO"

xlink:role="http://regrep.org/gci/purchaseOrder">

<Schema location="http://regrep.org/gci/purchaseOrder/po.xsd"

version="1.0"/>

</Reference>

</Manifest>

## Header element

The Header element immediately follows the Manifest element. It is REQUIRED in all ebXMLHeader documents. The Header element is a composite element comprised of the following subordinate elements:

From

To

CPAId

ConversationId

Service

Action

ReliableMessagingInfo

MessageData

#wildcard

The Header attribute MAY have an attribute: id that is of type XML ID.

### From and To elements

The From element identifies the Party that originated the message. It is a logical identifier, that MAY take the form of an URI. The From element consists of a PartyId element.

The To element identifies the intended recipient of the message. As with From, it is a logical identifier that is comprised of a PartyId element.

The PartyId element has a single attribute: type and a string value.

If the type attribute is present, then it indicates that the parties that are sending and receiving the message know, by some other means, how to interpret the content of the PartyId element. The two parties MAY use the value of the type attribute to assist in the interpretation.

If the type attribute is not present, the content of the PartyId element MUST be a URI [RFC 2396] otherwise there is an error.

The following fragment demonstrates usage of the From and To elements. The first illustrates a user-defined numbering scheme, and the second a urn.

<From>

<PartyId type="MyNumberingScheme">1234567890123</PartyId>

</From>

<To>

<PartyId">urn:dnb.com:duns:3210987654321</PartyId>

</To>

### CPAId element

The CPAId is a string that identifies the Collaboration Protocol Agreement that governs the processing of the message.  The CPAId MAY be an URI, possibly established by registering a CPA with the ebXML Registry, that identifies the CPA uniquely.

### ConversationId element

The ConversationId is a string that identifies the set of related messages that make up a conversation between two Parties. The Party that initiates a conversation determines the value of the ConversationId element that shall be reflected in all messages pertaining to that conversation.

Note that implementations are free to choose how they will identify and store conversational state related to a specific ConversationId. Implementations MUST provide a facility for mapping between their identification schema and a ConversationId generated by another implementation.

### Service element

The Service element identifies the service that SHOULD act on the payload in the message. It is specified by the designer of the service. The designer of the service may be:

a standards organization, or

an individual or enterprise

An URI MAY be used for the element content.

#### Type attribute

If the type attribute is present, then it indicates that the parties that are sending and receiving the message know, by some other means, how to interpret the content of the Service element. The two parties MAY use the value of the type attribute to assist in the interpretation.

If the type attribute is not present, the content of the Service element MUST be a URI [RFC 2396] otherwise there is an error.

#### ebXML Message Service Header namespace

URIs that start with the namespace: http://www.ebxml.org/namespaces/messageService are reserved for use by this specification.

### Action element

The Action identifies a process within a Service, that processes the Message. Action SHALL be unique within the Service in which it is defined.

### Description element

The Description element MAY be present as a child element of the Header. The language of the description is defined by a required xml:lang attribute. The xml:lang attribute MUST comply with the rules for identifying languages specified in [XML]. This element is provided solely for the purpose of providing a human readable description of the purpose or intent of the message.

### ReliableMessagingInfo element

The last element of the Header is the ReliableMessagingInfo element. This element identifies the quality of service with which the message MUST be delivered. This element has a single attribute, deliverySemantics. See section 9.2.3 for more details on how this element is used. An example of a ReliableMessagingInfo element follows.

<ReliableMessagingInfo deliverySemantics=”OnceAndOnlyOnce”/>

### MessageData element

The REQUIRED MessageData element follows the Action element within the Header element. The purpose of the MessageData element is to provide a means of uniquely identifying an ebXML Message. It is contains the following three elements:

MessageID

TimeStamp

RefToMessageID

#### MessageId element

The REQUIRED element MessageId is a unique identifier for the message conforming to [RFC2392]. The "local part" of the identifier as defined in [RFC2392] is implementation dependent.

#### TimeStamp element

The TimeStamp is a value representing the time that the message header was created conforming to [ISO-8601]. The format of CCYYMMDDTHHMMSS.SSSZ is REQUIRED to be used. This time format is Coordinated Universal Time (UTC).

#### RefToMessageId element

The RefToMessageId element has a cardinality of zero or one. When present, it MUST contain the MessageID value of an earlier ebXML Message to which this message relates. If there is no earlier message referenced, the element MUST NOT be present.

For Error messages, the RefToMessageId element is REQUIRED and its value MUST be the MessageId value of the message in error (as defined in section 8.8).

For Acknowledgment Messages, the RefToMessageId element is REQUIRED, and its value MUST be the MessageId value of the ebXML Message being acknowledged. See also sections 8.2.3.7 and 9.2.3.

### #wildcard element

In support of allowing an ebXML Message to be extended to include element content from a foreign namespace, a #wildcard element has been provided. Additional element content MAY be added to the Header element immediately following the MessageData element. Such additional element content MUST be namespace-qualified in accordance with [XMLNamespaces].

### Header sample

The following fragment demonstrates the structure of the Header element of the ebXMLHeader document:

<Header id="N01">

<From>

<PartyId type="uri">…</PartyId>

</From>

<To>

<PartyId type="userType">...</PartyId>

</To>

<CPAId>http://www.ebxml.org/cpa/123456</CPAId>

<ConversationId>987654321</ConversationId>

<Service>QuoteToCollect</Service>

<Action>NewPurchaseOrder</Action>

<ReliableMessagingInfo deliverySemantics="BestEffort"/>

<MessageData>

<MessageId>UUID-2</MessageId>

<TimeStamp>20000725T121905.000Z</TimeStamp>

<RefToMessageId>UUID-1</RefToMessageId>

</MessageData>

</Header>

## RoutingHeaderList element

A RoutingHeaderList consists of one or more RoutingHeader elements. Exactly one RoutingHeader is appended to the RoutingHeaderList, following any pre-existing RoutingHeader before transmission of a message over a data communication protocol.

The RoutingHeaderList element MAY be omitted from the header if:

the message is being sent over a single hop (see section 8.5.2), and

the message is not being sent reliably (see section 9.2.3)

### Routing Header Element

The RoutingHeader element contains information about a single transmission of a message between two Parties. If a message traverses multiple hops by passing through some type of intermediate system between the From Party and the To Party, then each transmission over each hop results in the addition of a new Routing Header element.

The RoutingHeader element is a composite element comprised of the following subordinate elements:

SenderURI

ReceiverURI

ErrorURI

Timestamp

#wildcard

#### SenderURI element

This element contains the URI of the messages’ Sender Messaging Service Handler. The recipient of the message, unless there is another URI more specifically identified within the CPA, uses the URI to send a message, when required that:

responds to an earlier message

acknowledges an earlier message

reports an error in an earlier message.

#### ReceiverURI element

This element contains is the URI of the Receiver’s Messaging Service Handler URI. It is the URI to which the Sender sends the message.

#### ErrorURI element

This URI, if present, identifies the URI that is used for reporting errors. If it is not present then errors are reported by sending a message to the SenderURI.

#### Timestamp element

The timestamp element is the time the individual RoutingHeader was created. It is in the same format as in the Timestamp element in the MessageData element.

#### #wildcard

This MAY contain any namespace-qualified element content belonging to a foreign namespace.

### Single Hop Routing Header Sample

A single hop message and its return is illustrated by the diagram below.

Figure 8-1 Single Hop Message

The content of the corresponding messages could include:

Transmission 1 - Message X From Party A To Party B

<Header id=”...”>

<From>urn:myscheme.com:id:PartyA-id</From>

<To>urn:myscheme.com:id:PartyB-id</From>

...

</Header>

<RoutingHeaderList id=”...”>

<RoutingHeader>

<SenderURI>url:PartyA.com/PartyAMsh</SenderURI>

<ReceiverURI>url:PartyB.com/PartyBMsh</ReceiverURI>

<Timestamp>20001216T21:19:35.145Z-8</Timestamp>

</RoutingHeader>

</RoutingHeaderList>

Transmission 2 - Message Y From Party B To Party A

<Header id=”...”>

<From>urn:myscheme.com:id:PartyB-id</From>

<To>urn:myscheme.com:id:PartyA-id</From>

...

</Header>

<RoutingHeaderList id=”...”>

<RoutingHeader>

<SenderURI>url:PartyA.com/PartyAMsh</SenderURI>

<ReceiverURI>url:PartyB.com/PartyBMsh</ReceiverURI>

<Timestamp>20001216T21:20:05.274Z-6</Timestamp>

</RoutingHeader>

</RoutingHeaderList>

### Multi-hop Routing Header Sample

Multi-hop messages are not sent directly from one party to another, instead they are sent via an intermediate party. This is illustrated by the diagram below.

Figure 8-1 Multi-hop Message

The content of the corresponding messages could include:

Transmission 1 - Message X From Party A To Party B

<Header id=”...”>

<From>urn:myscheme.com:id:PartyA-id</From>

<To>urn:myscheme.com:id:PartyC-id</From>

...

</Header>

<RoutingHeaderList id=”...”>

<RoutingHeader>

<SenderURI>url:PartyA.com/PartyAMsh</SenderURI>

<ReceiverURI>url:PartyB.com/PartyBMsh</ReceiverURI>

<Timestamp>20001216T21:19:35.145Z-8</Timestamp>

</RoutingHeader>

</RoutingHeaderList>

Transmission 2 - Message X From Party B To Party C

<Header id=”...”>

<From>urn:myscheme.com:id:PartyA-id</From>

<To>urn:myscheme.com:id:PartyC-id</From>

...

</Header>

<RoutingHeaderList id=”...”>

<RoutingHeader>

<SenderURI>url:PartyA.com/PartyAMsh</SenderURI>

<ReceiverURI>url:PartyB.com/PartyBMsh</ReceiverURI>

<Timestamp>20001216T21:19:35.145Z-8</Timestamp>

</RoutingHeader>

<RoutingHeader>

<SenderURI>url:PartyB.com/PartyAMsh</SenderURI>

<ReceiverURI>url:PartyC.com/PartyBMsh</ReceiverURI>

<Timestamp>20001216T21:19:45.483Z-6</Timestamp>

</RoutingHeader>

</RoutingHeaderList>

Message Y would be similar to Message X except that the direction of transmission is reversed.

## ApplicationHeaders Element

In support of allowing an ebXML Message to be extended to include application or implementation specific information, an ApplicationHeaders container element has been provided. Element content from a foreign namespace MAY be added to the ApplicationHeaders element. Such additional element content MUST be namespace-qualified in accordance with [XMLNamespaces].

An MSH implementation MUST make the information content of the ApplicationHeaders element available to the application or application services layer of software as described in the Service Interface section.

The ApplicationHeaders element has a single attribute: mustUnderstand. This attribute has two possible values: true and false. The default value for the mustUnderstand attribute is false. An ApplicationHeaders element that has a mustUnderstand set to a value of 'true' means that a receiving MSH MUST be capable of understanding the meaning of the namespace-qualified element content. If not, the receiving MSH MUST respond with a message that includes an error code of NotSupported  in an ErrorData element as defined in section 8.8.

### ApplicationHeaders sample

<ApplicationHeaders mustUnderstand="true">

<foo:ProprietaryStuff

xmlns:foo="http://www.example.com/ebxml-msh-extensions">…

</foo:ProprietaryStuff>

</ApplicationHeaders>

## StatusData Element

The StatusData element is used by one MSH to respond to a request on the status of the processing of a message that was previously sent (see also section 9.1).

The StatusData element consists of the following elements and attributes:

a RefToMessageId element that contains the MessageId of the message whose status is being checked

a ReceiptTimeStamp element. This contains the time that the message whose status is being checked was received. This MUST be omitted if the message whose status is being checked is NotRecognized or the request was UnAuthorized

a ForwardURI element. This MAY only be present if messageStatus is set to Forwarded. If present it indicates the URI of the ReceiverURI to which the message was forwarded

a messageStatus attribute that is set to one of the following values:

UnAuthorized – the Message Status Request is not authorized or accepted

NotRecognized – the message identified by the RefToMessageId element in the StatusData element is not recognized

Received – the message identified by the RefToMessageId element in the StatusData element has been received by the MSH, but has not been processed by an application or forwarded to another MSH

Processed – the message identified by the RefToMessageId element in the StatusData element has been received by the MSH for the To Party on the original message, and has been passed to the application or other process that is to handle it

Forwarded – the message identified by the RefToMessageId element in the StatusData element has been received by the MSH, and has been forwarded to another MSH

## ErrorList Element

The existence of an ErrorList element indicates that the message that is identified by the RefToMessageId in the header has an error.

The ErrorList element consists of one or more Error elements and the following two attributes:

id attribute

highestSeverity attribute

If there are no errors to be reported then the ErrorList element MUST NOT be present.

### id attribute

The id attribute uniquely identifies the ErrorHeader element within the document.

### highestSeverity attribute

The highestSeverity attribute contains the highest severity of any of the Error elements. Specifically, if any of the Error elements has a severity of Error then highestSeverity must be set to Error otherwise set highestSeverity to Warning.

### Error element

An Error element consists of the following:

codeContext attribute

errorCode attribute

severity attribute

location attribute

xml:lang attribute

errorMessage attribute

softwareDetails attribute

#### codeContext attribute

The codeContext attribute identifies the namespace or scheme for the errorCodes. It MUST be a URI. Its default value is http://www.ebxml.org/messageServiceErrors. If it is present then it indicates that an implementation of this specification has used its own errorCodes.

Use of non ebXML values for errorCodes is NOT RECOMMENDED. In addition, an implementation of this specification MUST NOT use its own errorCodes if an existing errorCode as defined in section 8.8.5 has the same or very similar meaning.

#### errorCode attribute

The required errorCode attribute indicates the nature of the error in the message in error. Valid values for the errorCode and a description of the code’s meaning are given in section 8.8.5.

#### severity attribute

The required severity attribute indicates the severity of the error. Valid values are:

Warning - This indicates that although there is a message in error other messages in the conversation will still be generated in the normal way.

Error - This indicates that there is an unrecoverable error in the message in error and no further messages will be generated as part of the conversation.

#### location attribute

The location attribute points to the part of the message that is in error.

If an error exists in the ebXML Header document and the document is “well formed” (see [XML]), then the content of the location attribute MUST be an [XPointer].

If the ebXML Header document is not “well formed” then the location attribute MUST be omitted.

If the error is associated with the MIME envelope that wraps the ebXML Header Document and the ebXML Payload, then location id contains the content-id of the MIME part that is in error, in the format cid:23912480wsr, where the text after the”:” is the value of the MIME part’s content-id.

The location attribute MUST NOT be used to point to errors inside the ebXML Payload Container as the method of reporting errors in the ebXML Payload Container is application dependent.

#### errorMessage atttribute

The errorMessage attribute provides a narrative description of the error in the language defined by the xml:lang attribute. Typically, it will be the message generated by the XML parser or other software that is validating the message. This means that the value of the attribute is defined by the vendor/developer of the software, that generated the Error element.

xml:lang must comply with the rules for identifying languages specified in [XML].

The errorMessage attribute MAY be omitted.

#### softwareDetails attribute

The softwareDetails attribute contains a value that is set by the vendor/developer of the software that generated the Error element. It SHOULD contain data that enables the vendor/developer as well as the recipient of the message to identify the precise location in their software and the set of circumstances that caused the software to generate a message reporting the error. It is RECOMMENDED that this element include plain text separated by punctuation to identify:

the name of the software vendor;

the name, version and release number of the software that generated the ebXML Error Document

the part of the software that caused the error to be generated that can be used by the Software Vendor to identify the circumstances that caused the error

If any part of the softwareDetails attribute contains text that is readable by a human, then it SHOULD be in the language identified by xml:lang.

### Examples

An example of an ErrorList element is given below.

<ErrorList id=’3490sdo9’, highestSeverity=”error”>

<Error errorCode=’UnableToParse’, severity=”Error”, location=cid:21398adhiwqe, xml:lang=”us-en”, errorMessage=’XSD parser error – document not parsable”, softwareDetails=’Software Development Corp.; ebXML Connector!!; v2.7, build 2.7313; Ref HA’/>

<Error .... />

</ErrorListr>

### errorCode values

This section describes the ErrorCodes (see section8.8.3.2) that are used in a message reporting an error. They are described as a list of bullet points. The following describes how to interpret this list:

the first word is the actual errorCode, e.g. UnableToParse

the single sentence that immediately follows the error code is an “error code description” of the errorCode. Note that this narrative MUST NOT be used in the errorMessage attribute.

the sentence(s) that follow the “narrative”, are the explanation of the meaning of the error and provide guidance on when the particular ErrorCode should be used.

It is RECOMMENDED that implementers of software that conforms to this specification make available to a user that is being informed of the error: the value of the errorCode, the “error code description” and the “narrative”.

It is also RECOMMENDED that the “error code description” and the “narrative” are translated into the preferred language of the user if this is known.

### Reporting Errors in the ebXML Header Document

The following list contains error codes that can be associated with the ebXML Header Document:

UnableToParse - XML not well formed or invalid. The XML document is not well formed or not valid and cannot be successfully parsed. See [XML] for the meaning of "well formed" and "not valid".

ValueNotRecognized - Element content or attribute value not recognized. Although the document is well formed and valid, the element/attribute contains a value that could not recognized and therefore could not be used by the ebXML Message Service

NotSupported - Element or attribute not supported. Although the document is well formed and valid, an element or attribute is present that:

is consistent with the rules and constraints contained in this specification, but

is not supported by the ebXML Message Service that is processing the message.

Inconsistent - Element content or attribute value inconsistent with other elements or attributes. Although the document is well formed and valid, according to the rules and constraints contained in this specification the content of an element or attribute is inconsistent with the content of other elements or their attributes.

OtherXml - Other error in an element content or attribute value. Although the document is well formed and valid, the element content or attribute value contains values that do not conform to the rules and constraints contained in this specification and is not covered by other error codes. The errorMessage attribute should be used to indicate the nature of the problem.

### Non-XML Document Errors

The following are error codes that identify errors that are not associated with the ebXML Header Document:

MessageTooLarge - Message too large. The message is too large to be processed by the ebXML Message Service.

MimeProblem - A MIME error has occurred. An error has been detected in the structure or format of a MIME part of the message. For example:

Missing MIME Part. Although the MIME message is correctly structured, a MIME part is missing that should have been present if the rules and constraints contained in this specification are followed

Unexpected MIME Part. Unexpected MIME part. Although the MIME message is correctly structured, a MIME part is present that is not expected in the particular context according to the rules and constraints contained in this specification

DeliveryFailure – Message Delivery Failure. A message has been received that either probably or definitely could not be sent to its next destination

TimeToLiveExpired – Message Time To Live Expired. A message has been received that arrived after the time specified in the TimeToLive element of the Header element

Unknown - Unknown Error. Indicates that an error has occurred that is not covered explicitly by any of the other errors. The errorMessage attribute should be used to indicate the nature of the problem.

Note this list will be expanded in future versions of this specification, for example to report errors on security. If the message being acknowledged was sent with deliverySemantics set to OnceAndOnlyOnce, then the acknowledgment message from the To Party might still arrive.

## Acknowledgment Element

The Acknowledgment element is an optional element that is used by one Party to indicate that another Party has received a message.  <CF>The use of Party in this context is going to be confusing! Some will think that a Business ack would be handled in this manner that I gather it would not be based on our discussions. I would suggest replacing party with MSH.</CF>

For clarity two terms are defined:

message being acknowledged. This is the Message that is has been received by a party that is now being acknowledged

acknowledgment message. This is the message that acknowledges that message being acknowledged has been receivedf.

The message being acknowledged is identified by the RefToMessageId contained in the MessageData element contained within the Header Element of the acknowledgment message containing the value of the MessageId of the message being acknowledged.

The Acknowledgment element consists of the following:

ReceiptTimeStamp element

From element

type attribute

signed attribute

### TimeStamp element

The TimeStamp element is a value representing the time that the message being acknowledged was received by the Party generating the acknowledgment message. It must conform to [ISO-8601]. The format of CCYYMMDDTHHMMSS.SSSZ is REQUIRED to be used. This time format is Coordinated Universal Time (UTC).

### From element

This is the same element as the From element defined in section 8.4.1. However, when used in the context of an Acknowledgment Element, it contains the identifier of the Party that is generating the acknowledgment message.

### type attribute

The type attribute indicates who sent the acknowledgment message. It MUST contain either:

DeliveryReceipt - indicates that the acknowledgment message was generated by the To Party identified by the To element of the message being acknowledged, or

IntermediateAcknowledgment - indicates that the acknowledgment message was generated by a Party that is not the To Party identified by the To element of the message being acknowledged. Typically this will be a Party that has received the message and is forwarding it to either the To Party or another Party with the intention that the message is sent to the To Party.

The default value for type is DeliveryReceipt.

### signed attribute

The signed attribute indicates whether the acknowledgment message is digitally signed. It MUST contain either:

True - indicates that the acknowledgment message is digitally signed, or

False - indicates that the acknowledgment message is not digitally signed

The default value for signed is False.

See section 12for details on what should be signed and how a signature that signs an acknowledgment message should be checked.

## Signature Element

TBD

# Message Service Handler Services

The Message Service Handler MUST support two services that are designed to help provide smooth operation of a Message Handling Service implementation:

Message Status Request

Message Service Handler Ping

Each service is described below:

## Message Status Request Service

The Message Status Request Service consists of the following:

sending a Message Status Request message to a MSH about a message previously sent

the Message Service Handler that receives the request sending a Message Status Response message in return.

### Message Status Request Message

A Message Status Request message consists of no ebXML Payload and the following elements in the ebXML Header:

A Header element

A RoutingHeaderList element

A Signature element

The RoutingHeaderList and the Signature elements MAY be omitted (see sections 8.5 and 8.10).

The Header element MUST contain the following:

a From element that identifies the creator of the message status request message

a To that identifies a Party that received the message. If a RoutingHeader was present on the message whose status is being checked then this MUST be a ReceiverURI from that message.

a Service element that contains: http://www.ebxml.org/namespaces/messageService/MessageStatus

an Action element that contains Request

The message is then sent to the To Party.

### Message Status Response Message

Once the To Party on the Message Status Request message receives the message, they MAY generate a Message Status Response message that consists of no ebXML Payload and the following elements in the ebXML Header.

a Header element

a RoutingHeaderList element

a Acknowledgement element

a StatusData element

a Signature element

The RoutingHeaderList, Acknowledgement and Signature elements MAY be omitted (see sections 8.5, 8.9 and 8.10).

The Header element MUST contain the following:

a From element that identifies the creator of the Message Status Response message

a To element that identifies a Party that generated the Message Status Request message

a Service element that contains: http://www.ebxml.org/namespaces/messageService/MessageStatus

an Action element that contains Response

a RefToMessageId that identifies the Message Status Request message.

The message is then sent to the To Party.

### Security Considerations

Party’s that receive a Message Status Request message SHOULD always respond to the message. However they MAY ignore the message instead of responding with messageStatus set to UnAuthorized if they consider that the sender of the message received is unauthorized. The decision process that results in this course of action is implementation dependent.

<DB> Do we want to allow the Message Status Response to include the original response to the message in the Payload?</DB><CF> quite possibly.</CF>

## Message Service Handler Ping Service

The Message Service Handler Ping Service enables one Message Service Handler to determine if another MSH is operating. It consists of:

sending a Message Service Handler Ping message to a MSH, and

the MSH that receives the Ping responding with a Message Service Handler Pong message.

### Message Service Handler Ping Message

A Message Service Handler Ping (MSH Ping) message consists of no ebXML Payload and the following elements in the ebXML Header:

A Header element

A RoutingHeaderList element

A Signature element

The RoutingHeaderList and the Signature elements MAY be omitted (see sections 8.5 and 8.10).

The Header element MUST contain the following:

a From element that identifies the creator of the MSH Ping message

a To element that identifies the operator of the MSH that is being sent the MSH Ping message

a Service element that contains: http://www.ebxml.org/namespaces/messageService/MSHStatus

an Action element that contains Ping

The message is then sent to the To Party.

### Message Service Handler Pong Message

Once the To Party on the MSH Ping message receives the message, they MAY generate a Message Service Handler Pong (MSH Pong) message that consists of no ebXML Payload and the following elements in the ebXML Header.

a Header element

a RoutingHeaderList element

an Acknowledgement element

a Signature element

The RoutingHeaderList, Acknowledgement and Signature elements MAY be omitted (see sections 8.5, 8.9 and 8.10).

The Header element MUST contain the following:

a From element that identifies the creator of the MSH Pong message

a To element that identifies a Party that generated the MSH Ping message

a Service element that contains: http://www.ebxml.org/namespaces/messageService/MessageStatus

an Action element that contains Pong

a RefToMessageId that identifies the MSH Ping message.

The message is then sent to the To Party.

### Security Considerations

Party’s that receive a MSH Ping message SHOULD always respond to the message. However there is a risk that some Parties might use the MSH Ping message to determine the existence of a Message Service Handler as part of a security attack on that MSH. Therefore recipients of a MSH Ping MAY ignore the message if they consider that the sender of the message received is unauthorized or part of some attack. The decision process that results in this course of action is implementation dependent.

# Reliable Messaging

Reliable Messaging defines an interoperable protocol such that the two Messaging Service Handlers operated by a From Party and a To Party can “reliably” exchange messages that are sent using “reliable messaging” semantics.

“Reliably” means that the From Party can be highly certain that the message sent will be delivered to the To Party. If there is a problem in sending a message then the sender resends the message until either the message is delivered, or the sender gives up. If the message cannot be delivered, for example because there has been a catastrophic failure of the To Party’s system, then the From Party is informed.

### Persistent Storage and System Failure

A MSH that supports Reliable Messaging MUST keep messages that are sent or received reliably in persistent storage. In this context persistent storage is a method of storing data that does not lose information after a system failure or interruption.

This specification recognizes that different degrees of resilience may be realized depending on the technology that is used to persist the data. However, as a minimum, persistent storage that has the resilience characteristics of a hard disk (or equivalent) SHOULD be used. It is strongly RECOMMENDED though that implementers of this specification use technology that is resilient to the failure of any single hardware or software component.

Even after a system interruption or failure, a MSH MUST ensure that messages in persistent storage are processed in the same way as if the system failure or interruption had not occurred. How this is done is an implementation decision.

### Methods of Implementing Reliable Messaging

ebXML support for Reliable Messaging can be implemented in one of two ways:

using the ebXML Reliable Messaging protocol, or

using commercial queuing transport protocol software products that are designed to provide reliable delivery of messages using proprietary protocols.

Each of these are described below.

## ebXML Reliable Messaging Protocol

The ebXML Reliable Messaging Protocol is used to implement Reliable Messaging when either:

no queuing transport protocol products are available, or

a decision has been made to use the ebXML Reliable Messaging Protocol on top of a queuing transport protocol.

Use of the ebXML Reliable Messaging Protocol is identified by the ReliableMessagingMethod parameter being set to ebXML (the default).

The remainder of this section describes the ebXML Reliable Messaging Protocol. In outline it involves:

a From Party sending a message to the To Party

the To Party returning another messages that references the first

This is illustrated by the figure below.

Figure 10-1 Indicating that a message has been received

The diagram above illustrates two terms that are used in the remainder of this section:

message being acknowledged. This is the Message that needs to be sent reliably and therefore needs to be acknowledged

acknowledgment message. This is the message that acknowledges that the message being acknowledged has been received.

The receipt of the acknowledgment message indicates that the message being acknowledged has been sent reliably.

A Message can be sent reliably either over:

a Single-hop i.e. the sending of a message directly from the From Party’s MSH to the To Party’s MSH without passing through any intermediate MSHs.

Multi-hops i.e. the sending of a message indirectly from the From Party’s MSH to the To Party’s MSH via an intermediate MSHs that is not owned by or operated by on behalf of either the From Party or the Two Party.

Multi-hop Reliable Messaging can work either with, or without, Intermediate Acknowledgments. See also section 8.5on Routing Headers

Single-hop Reliable Messaging is described first followed by Multi-hop Reliable Messaging. Note that Multi-hop Reliable Messaging is an extension of Single-hop reliable Messaging

### Single-hop Reliable Messaging

Single-hop Reliable Messaging is illustrated by Figure 6-1 above.

In Single-hop Reliable Messaging:

the From Party MSH sends to the To Party MSH, a message (the message being acknowledged) that contains:

a ReliableMessagingInfo element with deliverySemantics set to OnceAndOnlyOnce

a RoutingHeader element that identifies the sender and the receipient URIs

the To Party MSH returning to the From Party MSH, an acknowledgment message that contains:

a ReliableMessagingInfo element with deliverySemantics set to BestEfforts

an Acknowledgment element with type set to deliveryReceipt

#### Resending Lost Messages

This section describes the behavior that occurs when message are lost. For example, it is possible that a message being acknowledged was lost, for example:

Figure 10-1 Lost “Message Being Acknowledged”

... or that the Acknowledgment Message was lost, for example ...

Figure 10-2 Lost Acknowledgment Message

In either case the sender of the original Message (Message X in the diagram) must resend the original message in the way illustrated by the diagram below if reliable messaging is being used.

Figure 10-3 Resending Lost Messages

The diagram above shows the behavior that MUST be followed by the sender of the message being acknowledged (e.g. Message X) and the acknowledgment message (e.g. Message Y). Specifically:

- The sender of the message being acknowledged (e.g. Party A) MUST re-send the identical message to the To Party MSH if no Acknowledgment Message is received

- The recipient of the message being acknowledged (e.g. Party B), when it receives a duplicate message, MUST re-send to the sender of the message being acknowledged (e.g Party A), a message identical to the most recent message that was sent to the recipient (e.g. Party B)

- The recipient of the message being acknowledged (e.g. Party A) MUST ignore duplicate messages and not forward them a second time to the application, the next MSH or other process that ultimately needs to receive them.

In this context:

an identical message is a message that contains, apart from an additional RoutingHeader element, the same ebXML Header and ebXML Payload as the earlier message that was sent.

a duplicate message is a message that contains the same MessageId as an earlier message that was received.

the most recent message is the message with the latest Timestamp in the MessageData element that has the same RefToMessageId as the duplicate message that has just been received.

Note that the Communication Protocol Envelope MAY be different. This means that the same message MAY be sent using different communication protocols and the reliable messaging behavior described in this section will still apply. The ability to use alternative communication protocols is specified in the CPA.

#### Duplicate Acknowledgment Messages

The uncertain nature of the delivery of messages over the Internet means that the Party MSH sending the message being acknowledged must check for duplicate Acknowledgment Messages as the diagram below illustrates.

Figure 10-1 Handling Duplicate Acknowledgment Messages

In this example the message being acknowledged (message X) was delayed the first time it was sent (transmission 1). Meanwhile the message being acknowledged was resent by the sender (Party A) of the message being acknowledged (transmission 2) and processed by the recipient of the message being acknowledged (Party B) resulting in the acknowledgment message (message Y) being returned (tranmission 3). Later the original message being acknowledged from the sender of the message being acknowledged was received (transmission 4) and treated by the recipient of the message being acknowledged as a duplicate that meant that the recipient of the message being acknowledged resent the most recent message.

To support this, the sender of a Message being acknowledged MUST ignore duplicate Acknowledgment Messages with the same MessageId and not process them a second time.

### Multi-hop Reliable Messaging

Multi-hop reliable Messaging can occur either:

without Intermediate Acknowledgment, or

with Intermediate Acknowledgments

Each of these is described below.

#### Multi-hop Reliable Messaging without Intermediate Acknowledgments

Multi-hop Reliable Messaging without Intermediate Acknowledgment is identified by the IntermediateAckRequested of the Routing Header for the hop being set to False.

The overall message flow is illustrated by the diagram below.

Figure 10-1 Multi-hop Reliable Messaging without Intermediate Acknowledgments

This is essentially the same a Single-hop Reliable Messaging except that the Message passes through multiple intermediate parties. This means that:

the From Party (e.g. Party A) and the To Party (e.g. Party D) are the only parties that adopt the Reliable Messaging behavior described in this section

the intermediate parties (e.g. Parties B and C), just forward the messages they receive, they do not undertake any Reliable Messaging behavior.

It is RECOMMENDED that Multi-hop Reliable Messaging without Intermediate Acknowledgments is used when the From Party that is sending a message is confident that the sum of the times taken for ...

the message being acknowledged to be sent to the To Party, and

the acknowledgment message to be returned

... is sufficiently short so that the From Party will not resend the message being acknowledged.

This is described in more detail below:

- The From Party MSH (e.g. Party A) sends to an Intermediate Party (e.g. Party B) a message (the message being acknowledged) e.g. Message X in transmission 1, that contains

  - a ReliableMessagingInfo element with deliverySemantics set to OnceAndOnlyOnce

  - a RoutingHeader element that contains the SenderURI of the sender (e.g. the URL for Party A’s MSH) and the ReceiverURI of the next recipient of the message (e.g. the URL of Party B’s MSH)

Once the Intermediate Party (e.g. Party B or Party C), receives the message they determine its next destination (in the example above this could be done by the Routing Application) and forward the message (e.g. Transmission 2 of Message X) to the next Party (e.g. either Party C or Party D). Before sending the message they:

  - transfer elements in the ebXML Header and Payload unchanged from the inbound message to the outbound message except that, they

  - add a RoutingHeader element to the RoutingHeaderList that contains the SenderURI of the next party to receive the message (e.g. the URL for Party C’s or Party D’s MSH) and the ReceiverURI (e.g. the URL for Party B’s or Party C’s MSH)

The previous step then repeats until eventually the message (e.g. Message X) reaches its final destination at the To Party (e.g. Party D)

Once the To Party receives the message (i.e. the message being acknowledged) they return an acknowledgment message to the From Party through the Intermediate Parties. The acknowledgment message (e.g. Message Y in transmission 4) contains:

  - a RefToMessageId element that contains the MessageId of the message being acknowledged

  - a ReliableMessagingInfo element with deliverySemantics set to BestEfforts

  - an Acknowledgment element with type set to deliveryReceipt

  - a RoutingHeader element that contains the SenderURI of the sender (e.g. the URL for Party D’s MSH) and the ReceiverURI of the next recipient of the message (e.g. the URL of Party C’s MSH)

Steps 2 and 3 above then repeat until the acknowledgment message reaches the To Party (e.g. Party A)

#### Multi-hop Reliable Messaging with Intermediate Acknowledgments

Multi-hop Reliable Messaging with Intermediate Acknowledgments is similar to Multi-hop Reliable Messaging without Intermediate Acknowledgment except that any of the Parties that are transmitting a Message may request that the recipient return an Intermediate Acknowledgment.

This is illustrated by the diagram below.

Figure 10-1 Multi-hop Reliable Messaging with Intermediate Acknowledgments

The main difference between Multi-Hop Reliable Messaging with Intermediate Acknowledgments and the without is:

any party may request an intermediate acknowledgment

any party that either sends or receives a message that requests an intermediate acknowledgment must adopt the reliable messaging behavior even if the ReliableMessagingInfo element indicates otherwise.

It is RECOMMENDED that Multi-hop Reliable Messaging with Intermediate Acknowledgments is used when the From Party that is sending a message is considers that the sum of the times taken for ...

the message being acknowledged to be sent to the To Party, and

the acknowledgment message to be returned

... is so long that the From Party will resend the message being acknowledged.

The rules that apply to Multi-hop Reliable Messaging with Intermediate Acknowledgment are as follows:

- Any Party that is sending a message can request that the recipient send an Acknowledgment Message that is an Intermediate Acknowledgment by setting the IntermediateAckRequested of the RoutingHeader for the hop to True. (e.g Transmission 2 of Message X, or Transmission 6 of Message Y)

- If a MSH receives a message that is not the To Party that requires an Intermediate Acknowledgment (e.g. Transmission 2 of Message X, or Transmission 6 of Message Y) then:

  - If the MSH can identify itself as the ReceiverURI in the RoutingHeader for the hop, and

  - an Intermediate Acknowledgment is requested, then

  - the MSH must return an Acknowledgment Message (e.g. Transmission 3 of Message T, or Transmission 7 of Message U) with:

    - a RefToMessageId element that contains the MessageId of the message being acknowledged

    - a ReliableMessagingInfo element with deliverySemantics set to BestEfforts

    - an Acknowledgment element with type set to IntermediateAck

    - a RoutingHeader element that contains the SenderURI of the sender (e.g. the URL for Party C’s or Party B’s MSH) and the ReceiverURI of the next recipient of the message (e.g. the URL of Party B’s or Party C’s MSH)

  - Note. This applies even if the Reliable Messaging Info for the Message is set to BestEfforts

- If a MSH receives a message where it is To Party and it requires an Intermediate Acknowledgment (see step 2) then, unless the To Party is returning an Acknowledgment Message that is a Delivery Receipt, return an Acknowledgment Message as described in step 2c above.

## ebXML Reliable Messaging using Queuing Transports

This section describes the differences that apply if a Queuing Transport is used to implement Reliable Messaging.

Use of the ebXML Reliable Messaging Protocol is identified by the ReliableMessagingMethod parameter being set to Transport for Transmission (either a Single-hop or a Multi-hop)

If Reliable Messaging using a Queuing Transport is being used then the following rules apply:

- An Intermediate Ack SHOULD not be requested. If an Intermediate Ack is requested, then it is ignored.

- No message acknowledgments with an Acknowledgment element with a type of IntermediateAck should be sent, even if requested

- Implementations should use the facilities of the Queuing Transport to determine if the message was delivered

- If an intermediate MSH cannot forward message to the next Party then the From Party should be notified using the procedure described in section 10.4.

- An acknowledgment message with an Acknowledgment element with a type attribute set to deliveryReceipt may still be sent to inform the sender of the message being acknowledged that the message was delivered.

## Failed Message Delivery

It is possible, that a Message cannot be delivered to its ultimate destination. This can be either:

when the To Party MSH cannot deliver the message to the Application or other process that needs it, or

when using Intermediate Acknowledgments and an Intermediate system determines that a message may have been lost. This is illustrated by the diagram below.

Figure 10-1 Failed Message Delivery using Intermediate Acknowledgments

In this example, Party B does not know if Party C (or Party D) has received the message since, even after resending, it has not received the acknowledgment message (Message T).

In both these circumstances the MSH that detects the problem MUST send a message to the From Party that sent the message being acknowledged (via the Intermediate Party if required). The message contains:

a From Party that identifies the Party that detected the problem

a To Party that identifies the From Party that created the message that could not be delivered

a ReliableMessagingInfo element with deliverySemantics set to the same value as the deliverySemantics on the message that could not be delivered

an ErrorData element with a severity of:

Error if the Party that detected the problem could not even transmit the message (e.g. Transmission 3 was impossible)

Warning if the message (e.g. Message X in Transmission 4) was transmitted, but no acknowledgment was received. This means that the message probably was not delivered although there is a small probability that it was

an ErrorCode of DeliveryFailure

This is illustrated by the diagram below by the text and arrows in red.

Figure 10-2 Reporting Failed Message Delivery

Note that the message that contains an ErrorData element with an ErrorCode of DeliveryFailure (e.g. Message U in Transmission 7) might be sent reliably. It is possible the acknowledgment message for this message (e.g. Message V in Transmission 8) is not received. In this case, the Party that detects the failed delivery (e.g. Party B) SHOULD inform the Party (e.g. Party A) that sent the message being acknowledged (e.g. Message X in Transmission 1) of the failure. How this is done is outside the scope of this specification.

## Reliable Messaging Parameters

This section describes the parameters required to control reliable messaging. This parameter information may be contained:

in the ebXML Message header, or

in the CPA associated with the message.

If the information is in both the ebXML message header and the CPA, the information in the header over-rides the CPA.

### Who sets Message Service Parameters

The values to be used in parameters can be specified by the following parties:

the From Party

the To Party

the sending Message Service Handler (MSH)

the receiving Message Service Handler

Parameters set by the From Party or the To Party, apply to the delivery of a message as a whole. Parameters set by the sending or receiving MSH apply to a single-hop.

Note that the From Party is the sending MSH and the To Party is the receiving MSH for the first/last MSH that handles the message.

The table below indicates where these parameters may be set.

| Specified By | Parameter | CPA/ CPP | Message Header | Routing Header |
| --- | --- | --- | --- | --- |
| From Party | deliverySemantics | Yes | Yes | N/A |
| From Party | deliveryReceiptRequested | Yes | Yes | N/A |
| From Party | timeToLive | Yes | Yes | N/A |
| From Party | timeAccuracyRequired | Yes | No | No |
| To Party | deliveryReceiptProvided | Yes | No | No |
| Sending MSH | reliableMessagingMethod | No | N/A | Yes |
| Sending MSH | intermediateAckRequested | No | N/A | Yes |
| Sending MSH | timeout | Yes | No | No |
| Sending MSH | retries | Yes | No | No |
| Sending MSH | retryInterval | Yes | No | No |
| Receiving MSH | reliableMessagingSupported | Yes | No | No |
| Receiving MSH | intermediateAckSupported | Yes | No | No |
| Receiving MSH | persistDuration | Yes | No | No |
| Receiving MSH | mshTimeAccuracy | Yes | No | No |

In this table, the following interpretation of the columns should be used:

- the Specified By columns indicates the Party that sets the value in the Collaboration Party Protocol, Message Header, or Routing Header

if the CPA/CPP column contains a Yes then it indicates that the party in the Specified B column specifies the value that is present in the CPP

if the CPA/CPP column contains a No then it indicates that the parameter value is never specified in the CPP

if the Message Header/Routing Header columns contain a Yes then it indicates that the parameter value may be specified in the MessageHeader/Routing Header and over-rides any value in the CPA. It the value is not specified in the MessageHeader/Routing Header then the value in the CPA must be used.

if the Message Header/Routing Header columns contain a No then it indicates that the value in the CPA is always used

if the Message Header/Routing Header columns contain a N/A then it indicates that the value may be specified in another header

These parameters are described below.

### From Party Parameters

This section describes the parameters that are set by the From Party

#### Delivery Semantics

The deliverySemantics Parameter MUST used by the From Party to indicate whether the Message must be sent reliably. Valid Values are:

OnceAndOnlyOnce. The message must be sent using a reliableMessagingMethod that will result in the application or other process at the To Party receiving the message once and only once

BestEffort The reliable delivery semantics are not specified. In this case the value of reliableMessagingMethod is ignored.

If no value is provided for deliverySemantics then the default value is BestEffort.

If deliverySemantics is set to OnceAndOnlyOnce then if, for some reason a MSH cannot deliver the message to either directly or indirectly to the To Party MSH before TimeToLive has expired, then the MSH that detects the problem MUST send an Message to the From Party’s MSH indicating Delivery Failure. (See section 10.4)

If deliverySemantics is set to BestEffort then:

a MSH that received a message that it is unable to deliver MUST NOT take any action to recover or otherwise notify anyone of the problem, and

the MSH that sent the message must not attempt to recover from any failure.

This means that duplicate messages might be delivered to an application and persistent storage of messages is not required.

If the To Party is unable to support the type of Delivery Semantics requested, then the To Party SHOULD report the error to the From Party using an ErrorCode of NotSupported and a Severity of Error.

#### Delivery Receipt Requested

The deliveryReceiptRequested parameter MUST be used by a From Party to indicate whether a message should result in the To Party sending an acknowledgment message containing an Acknowledgment element with a type of deliveryReceipt in return.

The From Party SHOULD check the deliveryReceiptSupported parameter for the To Party before requesting a Delivery Receipt.

Valid values for deliveryReceiptRequested are:

Unsigned - requests that an unsigned Delivery Receipt is requeste4d

Signed - requests that a signed Delivery Receipt is requested, or

None - indicates that no Delivery Receipt is requested.

The default value is None.

If the To Party is unable to support the type of Delivery Receipt requested, then the To Party SHOULD report the error to the From Party using an ErrorCode of NotSupported and a Severity of Error.

#### Time To Live

TimeToLive is an optional element in the header that conforms to [ISO8601] and indicates the time by which a message should be delivered to the To Party MSH.

When setting a value for TimeToLive it is RECOMMENDED that the From Party takes into account the accuracy of its own internal clocks as well as the mshTimeAccuracy parameter for the Receiver MSH (see section 10.5.5.3) that indicates the accuracy to which a MSH will keep its internal clocks.

How a MSH ensures that its internal clocks are kept sufficiently accurate is an implementation decision.

Time To Live Expiry

If a MSH receives a Message where TimeToLive has expired the MSH MUST:

send a Message to the From Party MSH, reporting that the TimeToLive of the message has passed

NOT forward the message to another MSH or application/other system that should receive the message.

The message reporting the error MUST contain:

an ErrorCode set to TimeToLiveExpired

a severity attribute set to Error

In this context the TimeToLive has expired if the time of the internal clock of the MSH that receives a message is greater than the value TimeToLive for the Message

If TimeToLive is not present then it should be assumed that TimeToLive is infinite.

### To Party Parameters

This section describes the parameters that are set by the To Party

#### DeliveryReceiptProvided

The DeliveryReceiptProvided parameter indicates whether a To Party can provide an acknowledgment message with a type attribute of deliveryReceipt in response to a message. Valid values are:

Signed - indicates that only a signed Delivery Receipt can be provided

Unsigned - indicates only an unsigned Delivery Receipt can be provided,

Both - indicates that either a signed or an unsigned Delivery Receipt can be provided, or

None - indicates that the To Party does not create Delivery Receipts

If a MSH receives a Message where deliveryReceiptRequested is in not compatible with the value of DeliveryReceiptProvided then the MSH MUST return an Error Message to the From Party MSH, reporting that the DeliveryReceiptProvided is not supported. This must contain:

an ErrorCode set to NotSupported

a severity of Error

### Sending MSH Parameters

This section describes the parameters that are set by the Party that operates the Sending MSH.

#### Reliable Messaging Method

The ReliableMessagingMethod parameter indicates the requested method for Reliable Messaging that will be used when sending a Message. Valid values are:

ebXML in this case the reliable messaging method as defined in section 10.2 is followed, or

Transport, in this case a Queuing Transport Protocol is used for reliable delivery of the message. See also section 10.3.

#### Intermediate Ack Requested

The intermediateAckRequested parameter is used by the Sending MSH to request that the Receiving MSH that receives the Message to return an acknowledgment message with an Acknowledgment element with a type of IntemediateAck to the Sending MSH.

Valid values for intermediateAckRequested are:

Unsigned - requests that an unsigned Delivery Receipt is requested

Signed - requests that a signed Delivery Receipt is requested, or

None - indicates that no Delivery Receipt is requested.

The default value is None.

#### Timeout Parameter

The timeout parameter is an integer value that specifies the time in seconds that the Sending MSH MUST wait for an Acknowledgment Message before first resending a message to the Receiving MSH.

#### Retries Parameter

The retries Parameter is an integer value that specifies the maximum number of times the message being acknowledged must be resent to the Receiving MSH by the Sending MSH.

#### RetryInterval Parameter

The retryInterval parameter is an integer value specifying, in seconds, the time the Sending MSH MUST wait between retries, if an Acknowledgment Message is not received.

#### Deciding when to resend a message

The Sending MSH MUST resend the original message if an Acknowledgment Message has not been received from the Receiving MSH and either:

the message has not yet been resent and at least the time specified in the timeout parameter has passed since the first message was sent, or

the message has been resent, and

at least the time specified in the retryInterval has passed since the last time the message was resent, and

the message has been resent less than the number of times specified in the retries Parameter, and

If the Sending MSH does not receive an Acknowledgment Message after the maximum number of retries, the Sending MSH SHOULD notify either:

the application and/or system administrator function if the Sending MSH is the From Party MSH, or

send an message reporting the delivery failure, if the Sending MSH is operating by an Intermediate Party (see section 10.4)

### Receiving MSH Parameters

This section describes the parameters that are set by the Party that operates the Receiving MSH.

#### Reliable Messaging Methods Supported

The reliableMessagingMethodsSupported parameter is a list of the methods that a MSH uses to support Reliable Messaging. It must be a URI. The URI for the ebXML Reliable Messaging Protocol described in section 10.2 is http://www.ebxml.org/namespaces/reliableMessaging

#### PersistDuration

PersistDuration is the minimum length of time in days that a Message that is sent reliably is kept in Persistent Storage by a MSH. The value used for PersistDuration is an implementation decision although it MUST be greater than the value of the TimeToLive parameter for any message that is sent.

If a duplicate message (i.e. with the same MessageId) is received before the PersistDuration has passed, then the MSH that receives it MUST process it as a duplicate message as described in sections 10.2.1.1 and 10.2.1.2.

If a duplicate message is received after the PersistDuration has passed, then although it may be treated as a duplicate, the sender must realize that it will probably be treated by the MSH as if the message were a new message that had not been received before.

#### msh Time Accuracy

The mshTimeAccuracy parameter indicates the minimum accuracy that a Receiving MSH keeps the clocks it uses when checking, for example, TimeToLive. It’s value is in the format “mm:ss” where indicates the accuracy in minutes and seconds.

# Error Reporting and Handling

This section describes how one ebXML Message Service Handler (MSH) reports errors it detects in an ebXML Message to another MSH.

## Definitions

For clarity two phrases are defined that are used in this section:

message in error. A message that contains or causes an error of some kind

message reporting the error. A message that contains an ebXML Error List that describes the error(s) found in a message in error.

## Types of Errors

One MSH needs to report to another MSH errors in message in error that are associated with:

the structure or content of the Message Envelope (e.g. MIME),

the ebXML Message Header document,

security, or

reliable messaging failures.

Unless specified to the contrary, all references to "an error" in the remainder of this specification imply any of the types of errors listed above.

Errors associated with Data Communication protocols are detected and managed in an implementation specific way and are not part of this error reporting mechanism.

## When to generate Error Messages

When an MSH detects an error in a message in error, a message reporting the error MUST be generated and delivered to the MSH that sent the message in error if:

the Error Reporting Location (see section11.4) to which the message reporting the error should be sent can be determined, and

the message in error does not have an ErrorList element with highestSeverity set to Error.

If the Error Reporting Location cannot be found or the message in error has an ErrorList element with highestSeverity set to Error, it is RECOMMENDED that:

the error is logged,

the problem is resolved by other means, and

no further action is taken.

### Security Considerations

Party’s that receive a Message that contains an error in the header SHOULD always respond to the message. However they MAY ignore the message and not respond if they consider that the message received is unauthorized or is part of some security attack. The decision process that results in this course of action is implementation dependent.

## Identifying the Error Reporting Location

The Error Reporting Location is a URI that is specified by the sender of the message in error that indicates where to send a message reporting the error. This may be specified:

by reference, for example by using the CPAId to identify the Party Agreement that contains the Error Reporting Location, or

by value, for example by using the ErrorURI contained within the RoutingHeader element.

If a message contains both an ErrorURI then the ErrorURI MUST be used.

If an ErrorURI is not used then the ErrorURI implied by the CPA identified by the CPAid on the message SHOULD be used. If no ErrorURI is implied by the CPA, then the SenderURI MUST be used.

Even if the message in error cannot be successfully analyzed or parsed, MSH implementers SHOULD try to determine the Error Reporting Location by other means. How this is done is an implementation decision.

# Security

The ebXML Message Service, by its very nature, presents certain security risks. A Message Service may be at risk by means of:

Unauthorized access

Data integrity and/or confidentiality attacks (e.g. through man-in-the-middle attacks)

Denial-of-Service, spoofing, bombing attacks

Each of these security risks MAY be addressed in whole, or in part, by the application of one, or a combination, of the countermeasures described in this section. This specification describes a set of profiles, or combinations of selected countermeasures, that have been selected to address key risks based upon commonly available technologies. Each of the specified profiles includes a description of the risks that are not addressed.

Application of countermeasures SHOULD be balanced against an assessment of the inherent risks and the value of the asset(s) that might be placed at risk. <CF> need some reference to risk assessment sites/docs here.</CF>

## Security and Management

No technology, regardless of how advanced it might be, is an adequate substitute to the effective application of security management policies and practices.

It is STRONGLY RECOMMENDED that the site manager of an ebXML Message Service apply due diligence to the support and maintenance of its; security mechanism, site (or physical) security procedures,  cryptographic protocols, update implementations and apply fixes as appropriate. (See http://www.cert.org/ ,http://ciac.llnl.gov/)

## Collaboration Party Profiles

The configuration of Security for MSH’s is specified in the CPP.  There are three areas of the CPP that have security definitions as follows:

The DocumentExchange section addresses security to be applied to the payload of the message.  The MSH is not responsible for any security specified at this level but may offer these services to the message sender.

The Message section addresses security applied to the entire ebXML Document, which includes the header and the payload.

The Transport section addresses the Transport level.  The MSH is not responsible for any security specified at this level.

## RISKS

### Unauthorized Access

One of the risks for Message Service Handlers is sending messages to or receiving messages from another message service handler that is not known or one that is being impersonated by a rogue MSH. Receiving a flood of requests from a known or unknown MSH can be considered a denial of service attack.  Message Service Handlers need to be identified and need to be able to authenticate requests from other MSH’s.

A message MAY carry information that authenticates the sending MSH in the message header.  If authentication data is in the header, it MUST be protected from modification and inappropriate access.

Messages that are digitally signed MAY also be asserted as authenticated requests.

Authentication MAY also be provided by the underlying transport, such as through the use of [TLS].

### Data Integrity and Confidentiality

Integrity protection is the term used to express a requirement that data MUST be protected from unauthorized modification while it is stored or passed over the network.  The common technology for integrity protection is to generate  a hash of the data  and storing both the information and the hash securely. In a network protocol the hash is sent through a protected means and MAY be used to validate that the data received is the same data that was sent.

Privacy, or confidentiality, is the term used to express a requirement that data MUST be encrypted while it is stored or passed over the network.  The common method for privacy protection is encryption via symmetric key algorithm like DES or triple-DES.

### Denial-of Service

It is assumed that ebXML data and operations flow over the existing web infrastructure. All message services will implement their own web security infrastructure and practices. There are threats at all levels of the stack that need to be addressed through other means outside ebXML.

## CounterMeasure Technologies

### ebXML Message Countermeasures for  Unauthorized Access and Data Integrity

### Digital Certificates

The X.509 v3 standard describes an extensible framework within which basic certificate information MAY be extended. It also describes how such extensions MAY be used to control the process of issuing and validating certificates. Presently, there is no single view as to which certificate extensions must be present in an X.509 v3 digital certificate. The Collaboration Protocol Agreement identifies the particular X.509 v.3 certificate extensions that the parties to an agreement have agreed to use. An implementation of the ebXML Message Service MAY handle the subset of the certificate extensions listed in [S/MIME], but this capability is NOT REQUIRED. A Message Service that receives a message that contains critical extensions in an X509 v3 certificate that it is unable to handle MUST abandon processing of the message and return an Error XXX.

An implementation of the ebXML Message Service MAY implement a certificate-revocation list (CRL) retrieval mechanism. The purpose of a CRL is to gain access to certificate revocation information when validating certificate chains. It is RECOMMENDED that the Message Service retrieve and utilize CRL information each time a certificate is verified. The ultimate decision regarding use of the CRL information is left to the security policy of a party deploying an ebXML Message Service.

The use of a digital signature on an ebXML message satisfies the requirements for message integrity verification as well as authentication of the sender’s identity. The digital signature also helps to establish the ebXML message non-repudiation property.

### ebXML Message Countermeasures for Denial of Service

Message Service implementations SHOULD be able to immediately detect messages that MAY be a denial of service attack and take appropriate measures to reject these messages. Message Service implementations SHOULD be able to authenticate the claimed identity of a message sender when authentication is REQUIRED by the business.

### ebXML Management Countermeasures for Denial of Service

It is STRONGLY RECOMMENDED that the site manager of an ebXML Message Service take appropriate measures to monitor announcements and descriptions of new attacks (See http://www.cert.org/ ) and apply updates and patches as appropriate.

## Profiles

### XML Digital Signature (XMLDSIG)

The joint W3C/IETF XMLDSIG Working Group has released the [XMLDSIG] specification as a Candidate Recommendation effective November, 2000. This means that the specification is made public for the purposes of encouraging implementations of the specification to validate that it can be successfully implemented. To date, there are at least three implementations of the specification in circulation, with others under development. It is anticipated that this specification, along with the recently initiated XML Encryption Working Group (also a joint W3C/IETF initiative) will be key technologies that MAY be employed by the ebXML Message Service.

The [XMLDSIG] specification defines how an XML document(s) MAY be signed, either in whole or as selective element content by means of a transformation such as [XPATH] or [XSLT].

### Profile - XMLSignature signing of header and/or payload

An ebXML Message MAY be signed using technology that implements the [XMLDSIG] specification.

Blah blah blah blah, yadda yadda yadda.

#### Risks

This profile does not provide persistent privacy/confidentiality. It is STRONGLY RECOMMENDED that this profile be used in conjunction with a secure transport that provides for authentication as well as encryption over the network such as is provided by [TLS]. HTTP over SSL (HTTP/S) would be such a transport mechanism.

#### Benefits

This profile provides the only means of signing both the header and payload objects. This profile also allows the message to be modified as it traverses through intermediary Message Service Handlers that MUST append RoutingHeader elements as the message is (re) sent on its path from the From Party to the To Party.

### S/MIME

[S/MIME] names the message digest algorithms (md5, sha1), the public key encryption algorithm (RSA), and the bulk data encryption algorithms (RC2/40 and, optionally, Triple DES) that MUST be implemented in order to comply with the standard. An implementation of the ebXML Message Service that claims support for S/MIME SHALL conform to that standard.

The [S/MIME] specification REQUIRES that each MIME entity to be signed and/or encrypted MUST be converted to a canonical form that may be uniquely and unambiguously represented in both the environment where the signature is to be created and the environment where the signature is to be verified. MIME entities MUST be presented in a canonical format for enveloping as well as for signing.

The S/MIME specification RECOMMENDS transmitting entities such as 8-bit text and binary data to be encoded with quoted-printable or base-64 transfer encoding. This provision applies to formatting of the ebXML messages due to the transport independence property of the protocol.

Digital certificates are delivered as a part of the application/pkcs7-signature part of the multipart/signed message. [S/MIMECH] provides the guidelines for use of the digital certificates in S/MIME messages. The exact implementation of the certificate handling procedures and authentication semantics of the information in the digital certificate received with an ebXML message is left to the Trading Partner Agreement. <CF> this needs work!</CF>

### Profile - S/MIME signing of message payload

The multipart/signed form defined by the [S/MIME] specification MAY be used to sign ebXML message payloads. This specification makes no claims as to how the signing and packaging of the payload object(s) is to be achieved. An implementation of the ebXML Message Service MAY choose to offer these services to the application or application service layers of software as described in the section on the Message Service Interface. However, this is not a REQUIRED feature of an ebXML Message Service.

This profile SHALL be uniquely identified by the following URI:

http://www.ebxml.org/namespaces/security-profiles/smime-pkcs7-signed-payload

The [S/MIME] specification REQUIRES two parameters of the multipart/signed content type:

protocol

micalg

An ebXML message payload that is signed using this profile SHALL use the following values for these MIME parameters:

protocol="application/pkcs7-signature

micalg="rsa-sha1"

#### Sample S/MIME signed payload

Content-Type: multipart/related; type="application/vnd.eb+xml; version="0.9"; boundary=ebxmlenvelopeuniquestring;

Content-Id: localpart@domain

--ebxmlenvelopeuniquestring

Content-Type: application/vnd.eb+xml; version="0.9"; charset="UTF-8";

Content-Id: localpart@domain

<?xml version="1.0" encoding="UTF-8"?>

<ebXMLHeader version="0.9" xmlns=http://www.ebxml.org/namespaces/messageHeader>

…

</ebXMLHeader>

--ebxmlenvelopeuniquestring

Content-Type: multipart/signed; boundary="someuniquestring"; protocol="application/pkcs7-signature"; micalg="rsa-sha1";

Content-Id: localpart@domain

--someuniquestring

Content-Type: text/plain

Content-Id: localpart@domain

<Payload in the clear>

--someuniquestring

Content-Type: application/pkcs7-signed; name="smime.p7s";

Content-Id: localpart@domain

Content-Transfer-Encoding: base64

%^)*&TLYGSRKWHF

--someuniquestring--

--ebxmlenvelopeuniquestring--

#### Risks

This profile does not provide persistent privacy/confidentiality. It is STRONGLY RECOMMENDED that this profile be used in conjunction with a secure transport that provides for authentication as well as encryption over the network such as is provided by [TLS]. HTTP over SSL (HTTP/S) would be such a transport mechanism.

The header document is unsigned and there is no binding of the header and payload.

#### Benefits

This is the simplest form of integrity, with application signing and authentication of the payload only.

### Profile - S/MIME encryption of message payload

This profile SHALL be uniquely identified by the following URI:

http://www.ebxml.org/namespaces/security-profiles/smime-pkcs7-encrypted-payload

The [S/MIME] specification REQUIRES two parameters of the multipart/signed content type:

protocol

micalg

An ebXML message payload that is signed using this profile SHALL use the following values for these MIME parameters:

protocol="application/pkcs7-signature

micalg="rsa-sha1"

#### Risks

The header document is unsigned and there is no binding of the header and payload.

#### Benefits

This is the simplest form of integrity, with application signing and authentication of the payload only.

### PGP/MIME

[PGP/MIME] MAY be used to sign and/or encrypt an ebXML message payload object(s). An implementation of the ebXML Message Service that claims support for PGP/MIME SHALL conform to that standard.

### Profile - PGP/MIME signing of message payload

TBD - Dick

#### Risks

This profile does not provide persistent privacy/confidentiality. It is STRONGLY RECOMMENDED that this profile be used in conjunction with a secure transport that provides for authentication as well as encryption over the network such as is provided by [TLS]. HTTP over SSL (HTTP/S) would be such a transport mechanism.

The header document is unsigned and there is no binding of the header and payload.

#### Benefits

### Profile - PGP/MIME encryption of message payload

TBD - Dick

#### Risks

#### Benefits

# Synchronous and Asynchronous Responses

# References

## Normative References

[ISO 8601]	International Standards Organization Ref. ISO 8601 Second Edition, Published 1997

[RFC 2392] 	IETF Request For Comments 2392. Content-ID and Message-ID Uniform Resource Locators. E. Levinson, Published August 1998

[RFC2045]	IETF RFC 2045. Multipurpose Internet Mail Extensions (MIME) Part One: Format of Internet Message Bodies, N Freed & N Borenstein, Published November 1996

[RFC 2396]

[UTF-8]	UTF-8 is an encoding that conforms to ISO/IEC 10646. See [XML] for usage conventions.

[XML Namespace] Recommendation for Namespaces in XML, World Wide Web Consortium, 14 January 1999, http://www.w3.org/TR/REC-xml-names

[TLS]	RFC2246, T. Dierks, C. Allen. January 1999.

[XML]	W3C XML 1.0 Recommendation,
http://www.w3.org/TR/2000/REC-xml-20001006

[SMTP]	RFC 821, Simple Mail Transfer Protocol, J Postel, August 1982

[HTTP]	RFC 2068 - Hypertext Transfer Protocol -- HTTP/1.1, R. Fielding, J. Gettys, J. Mogul, H. Frystyk, T. Berners-Lee, January 1997

## Non-Normative References

[Glossary]	ebXML Glossary, see ebXML Project Team Home Page

[XMTP]	XMTP - Extensible Mail Transport Protocol http://www.openhealth.org/documents/xmtp.htm

[TRPREQ]	ebXML Transport, Routing and Packaging: Overview and Requirements, Version 0.96, Published 25 May 2000

[XMLMedia]	IETF Internet Draft on XML Media Types. See http://www.imc.org/draft-murata-xml-08. Note. It is anticipated that this Internet Draft will soon become a RFC. Final versions of this specification will refer to the equivalent RFC.

[XMLSchema]	W3C XML Schema Candidate Recommendation,
http://www.w3.org/TR/xmlschema-0/
http://www.w3.org/TR/xmlschema-1/ 
http://www.w3.org/TR/xmlschema-2/

[XMLDSIG]	Joint W3C/IETF XML Digital Signature specification,
http://www.w3.org/TR/2000/CR-xmldsig-core-20001031/

[XLINK]	W3C Xlink Candidate Recommendation, http://www.w3.org/TR/xlink/

[S/MIME]	RFC2311, “S/MIME Version 2 Message Specification”, S. Dusse, P. Hoffman, B.Ramsdell, L. Lundblade, L. Repka. March 1998.

[S/MIMECH]	RFC 2312, “S/MIME Version 2 Certificate Handling”, S. Dusse, P. Hoffman, B. Ramsdell, J. Weinstein. March 1998.

[PGP/MIME]	RFC2015, "MIME Security with Pretty Good Privacy (PGP)", M. Elkins. October 1996.

# Disclaimer

The views and specification expressed in this document are those of the authors and are not necessarily those of their employers. The authors and their employers specifically disclaim responsibility for any problems arising from correct or incorrect implementation or use of this design.

# Contact Information

Team Leader

Name 			Rik Drummond

Company 		Drummond Group, Inc.

Street 			5008 Bentwood Crt.

City, State, Postal Code Fort Worth, Texas 76132

Country 		USA

Phone 			+1 (817) 294-7339

EMail 			rik@drummondgroup.com

Vice Team Leader

Name 			Chris Ferris

Company 		Sun Microsystems

Street 			One Network Drive

City, State, Postal Code Burlington, MA 01803-0903

Country 		USA

Phone: 			+1 (781) 442-3063

EMail: 			chris.ferris@sun.com

Team Editor

Name 			David Burdett

Company 		Commerce One

Street			4400 Rosewood Drive

City, State, Postal Code Pleasanton, CA 94588

Country 		USA

Phone: 			+1 (925) 520-4422

EMail: 			david.burdett@commerceone.com

Authors

Name 			Dick Brooks

Company 		Group 8760

Street 			110 12th Street North, Suite F103

City, State, Postal Code Birmingham, Alabama 35203

Phone: 			+1 (205) 250-8053

E-mail: 			dick@8760.com

Name 			David Burdett

Company 		Commerce One

Street 			4400 Rosewood Drive

City, State, Postal Code Pleasanton, CA 94588

Country 		USA

Phone: 			+1 (925) 520-4422

EMail: 			david.burdett@commerceone.com

Name 			Chris Ferris

Company 		Sun Microsystems

Street 			One Network Drive

City, State, Postal Code Burlington, MA 01803-0903

Country 		USA

Phone: 			+1 (781) 442-3063

EMail: 			chris.ferris@east.sun.com

Name 			John Ibbotson

Company 		IBM UK Ltd

Street 			Hursley Park

City, State, Postal Code Winchester SO21 2JN

Country 		United Kingdom

Phone: 			+44 (1962) 815188

Email: 			john_ibbotson@uk.ibm.com

Name 			Nicholas Kassem

Company 		Java Software, Sun Microsystems

Street 			901 San Antonio Road, MS CUP02-201

City, State, Postal Code Palo Alto, CA 94303-4900

Phone: 			+1 (408) 863-3535

E-mail: 			Nick.Kassem@eng.sun.com

Name 			Masayoshi Shimamura

Company 		Fujitsu Limited

Street 			Shinyokohama Nikko Bldg., 15-16, Shinyokohama 2-chome

City, State, Postal Code Kohoku-ku, Yokohama 222-0033, Japan

Phone: 			+81-45-476-4590

E-mail: 			shima@rp.open.cs.fujitsu.co.jp

Document Editing Team

Name 			Ralph Berwanger

Company 		bTrade.com

Street 			2324 Gateway Drive

City, State, Postal Code Irving, TX 75063

Country 		USA

Phone: 			+1 (972) 580-2900

EMail: 			rberwanger@btrade.com

Name 			Ian Jones

Company 		British Telecommunications

Street 			Enterprise House, 84-85 Adam Street

City, State, Postal Code Cardiff, CF24 2XF

Country 		United Kingdom

Phone: 			+44 29 2072 4063

EMail: 			ian.c.jones@bt.com

Name 			Martha Warfelt

Company 		Daimler Chrysler Corporation

Street 			800 Chrysler Drive

City, State, Postal Code Auburn Hills, MI

Country 		USA

Phone: 			+1 (248) 944-5481 1210

EMail: 			maw2@daimlerchrysler.com 1211

Schema and Data Type Definitions

Schema Definition

Data Type Definition

Examples

Communication Protocol Interfaces

This Appendix describes how the ebXML Message Service messages are carried by Communication Protocols. Two protocols are supported:

Hypertext Transfer Protocol – HTTP/1.1, in both asynchronous and synchronous forms, and

SMTP – Simple Mail Transfer Protocol

HTTP

This section describes how to transport ebXML compliant messages of [HTTP]. This can work in one of the following two ways:

asynchronously, where the response to a message is sent using a separate HTTP POST, and

synchronously, where the response to a message is sent on the HTTP RESPONSE returned from an HTTP POST

These are described below.

Asynchronous HTTP

In Asynchronous HTTP, all ebXML Message Service messages are carried by an HTTP Request Message (POST method). The HTTP Response Message to an HTTP Request Message has no entity body. This is illustrated by the figure below.

Figure C.1  Asynchronous HTTP Message Flow

A message that is being sent asynchronously MAY be identified by the following HTTP header:

ebxmlresponse=asynchronous

If the ebXMLresponse HTTP parameter is omitted then it MUST be assumed that the response is sent asynchronously.

Synchronous HTTP

In Synchronous HTTP, one ebXML Message Service message is carried by an HTTP Request Message (POST method) with the ebXML Message that is a response to the first message sent in the HTTP Response Message to the HTTP Request Message. This is illustrated by the figure below.

Figure C.2  Synchronous HTTP Message Flow

If a response is being sent synchronously, the following HTTP header MUST be included in the HTTP envelope:

ebxmlresponse=synchronous

SMTP

All ebXML Message Service messages are carried as mail in an [SMTP] Mail Transaction as shown in the figure below.

Figure C.3 SMTP Message Flow

The Mail Transaction follows RFC 821, “SIMPLE MAIL TRANSFER PROTOCOL”, as shown in the following Figure:

Figure C.4	 SMTP Sequence

FTP

This section will describe how ebXML Messages may be sent using the File Transfer protocol as defined in RFC 959

This section to be completed.

Communication Protocol Errors during Reliable Messaging

When the Sender or the Receiver detects a transport protocol level error (such as an HTTP, SMTP or FTP error), the appropriate transport recovery handler will execute a recovery sequence. No Reliable Messaging functions (see section 9.2.3) are involved in this recovery sequence, since it happens at a lower level.

However, if the Sender detects a transport protocol level error that is unrecoverable at the transport protocol level, the appropriate recovery handler in the Sender will execute a Messaging Service recovery sequence as described in section 9.2.3.

<DB>Do we need to provide more detail for HTTP errors that are synchronous. For example if there is an ebXML error, do you respond with a 400?</DB>

Reliable Messaging Processing Logic

This section will contain non-normative reference processing logic to describe the behavior of a MSH that is taking part in reliable messaging. It’s purpose is to assist implementers in developing consistent interoperable solutions.

# Copyright Statement

This document and translations of it may be copied and furnished to others, and derivative works that comment on or otherwise explain it or assist in its implementation may be prepared, copied, published and distributed, in whole or in part, without restriction of any kind, provided that the above copyright notice and this paragraph are included on all such copies and derivative works. However, this document itself may not be modified in any way, such as by removing the copyright notice or references to the Internet Society or other Internet organizations, except as needed for the purpose of developing Internet standards in which case the procedures for copyrights defined in the Internet Standards process must be followed, or as required to translate it into languages other than English.

The limited permissions granted above are perpetual and will not be revoked by ebXML or its successors or assigns.

This document and the information contained herein is provided on an "AS IS" basis and ebXML DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF THE INFORMATION HEREIN WILL NOT INFRINGE ANY RIGHTS OR ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.

# Comments

General Security & Management recommendations

new text

need to tie this in to requirements in the CPP for authenticating at the MSH or transport level.